## Slide 1: Arithmetic for Binary Computers (ABCs) Integers
Programming at the Hardware/Software Interface

## Slide 2
You are free to:
Share — copy and redistribute the material in any medium or format
Adapt — remix, transform, and build upon the material for any purpose, even commercially
Under the following terms:
Attribution — You must give appropriate credit, provide a link to the license, and indicate if changes were made. You may do so in any reasonable manner, but not in any way that suggests the licensor endorses you or your use.
No additional restrictions — You may not apply legal terms or technological measures that legally restrict others from doing anything the license permits.
Slide by Bohn
This work is licensed under a Creative Commons Attribution 4.0 International License. This work is ©2018-21 Christopher A. Bohn, bohn@unl.edu.
These lecture slides are meant to enhance your use of the Programming at the Hardware/Software Interface textbook. If you have not adopted this publication for your course, please consider doing so.

## Slide 3: Unsigned Integers

## Slide 4: Encoding Integers
Slide by Bohn

## Slide 5: Encoding Integers
Slide by Bohn
Notes: On the next slide, we do a sanity check for converting binary to hex

## Slide 6: Encoding Integers
Slide by Bohn

## Slide 7: Bit-level representation, by type size
Type | Size | Binary | Hexadecimal
unsigned char | 8 bits | 1110 0111 | E7
unsigned short | 16 bits | 0000 0000 1110 0111 | 00 E7
unsigned int | 32 bits | 0000 0000 0000 0000 0000 0000 1110 0111 | 00 00 00 E7
unsigned long | 64 bits | 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 1110 0111 | 00 00 00 00 00 00 00 E7
Slide by Bohn
Representation of 23110
assuming 64-bit processor
Type | Size | Binary | Hexadecimal
unsigned char | 8 bits | (insufficient bits) | 
unsigned short | 16 bits | 0000 0111 1110 0101 | 07 E5
unsigned int | 32 bits | 0000 0000 0000 0000 0000 0111 1110 0101 | 00 00 07 E5
unsigned long | 64 bits | 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0111 1110 0101 | 00 00 00 00 00 00 07 E5
Representation of 202110

## Slide 8: Bit-level representation, by type size
Type | Size | Binary | Hexadecimal
unsigned char | 8 bits | (insufficient bits) | 
unsigned short | 16 bits | (insufficient bits) | 
unsigned int | 32 bits | 0000 0000 0000 0001 0000 1011 1110 1100 | 00 01 0B EC
unsigned long | 64 bits | 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0001 0000 1011 1110 1100 | 00 00 00 00 00 01 0B EC
Slide by Bohn
Representation of 6858810
assuming 64-bit processor

## Slide 9: Maximum Values, by type size
Constant | Value
UCHAR_MAX | 255
USHORT_MAX | 65,535
UINT_MAX | 4,294,967,295U
ULONG_MAX | 18,446,744,073,709,551,615UL
Constants defined in <limits.h>
Values are platform-specific
Useful, if used correctly
Use uint8_t, uint16_t, etc. if number of bits is critical
  Defined in <stdint.h>
Slide by Bohn
assuming 64-bit processor
Suffixes U, UL not to treat these as signed int (default for constants)
Notes: What do I mean by “if used correctly”?

## Slide 10: “if used correctly”
/* print every valid
* unsigned short value */
unsigned short s = 0;
while (s <= USHORT_MAX) {
printf("%d\n”, s++);
}
/* print every valid
* unsigned short value */
unsigned short s = 0;
while (s < USHORT_MAX) {
printf("%d\n”, s++);
}
printf("%d\n”, s);
Slide by Bohn
WILL NEVER TERMINATE!
Notes: (gosh) Why won’t the first example terminate? Well…

## Slide 11: Unsigned Addition
n+1 bits
Add two n-bit integers
Potentially need n+1 bits for sum
Only have n bits available for sum
Truncate carry-out
Implements modular arithmetic
Slide by Bohn
. . .
. . .
. . .
a
b
a+b
n bits
n bits
+1

## Slide 12: Difference between Z and integer types
Slide by Bohn
Traditional Z number line
… -3 -2 -1 0 1 2 3 …
Bit-limited
number circle
00..00
00..01
00..10
01..01
01..10
01..11
. . .
. . .
11..01
10..10
11..10
10..01
11..11
10..00
ADD
SUBTRACT

## Slide 13: Addition: Unsigned Integer Overflow
Slide by Bohn
Bit-limited
number circle
00..00
00..01
00..10
01..01
01..10
01..11
. . .
. . .
11..01
10..10
11..10
10..01
11..11
10..00
ADD
SUBTRACT
65533
65533 + 5 = ?
True Sum: 65533 + 5 = 65538
16 bit Sum:
65533 + 5 = 2
65534
65535
0
1
2
65533 + 5 mod 65536 = 2
Notes: 65533 + 5
65534 + 4
65535 + 3
65536 – oops!
0 + 2
1 + 1
2 + 0

## Slide 14: Addition: Ripple-Carry Adder
Slide by Bohn
1-bit Full Adder
A
B
Cin
Cout
(A&B) | ((A^B)&Cin)
Sum
(A^B)^Cin

## Slide 15: Addition: Ripple-Carry Adder
Slide by Bohn
1-bit Full Adder
A0
B0
0
Sum0
1-bit Full Adder
A1
B1
Sum1
carry
carry
1-bit Full Adder
A2
B2
Sum2
1-bit Full Adder
A3
B3
Sum3
carry
carry
(n.b.: carry-lookahead adder much faster but also much more complex)

## Slide 16: Addition: Detecting Unsigned Integer Overflow
Slide by Bohn
1-bit Full Adder
A0
B0
0
Sum0
1-bit Full Adder
A1
B1
Sum1
carry
carry
1-bit Full Adder
A2
B2
Sum2
1-bit Full Adder
A3
B3
Sum3
carry
carry
(n.b.: carry-lookahead adder much faster but also much more complex)
If Cout_n-1 = Cin_0 then unsigned addition overflowed

## Slide 17: Signed Integers

## Slide 18: Encoding Integers: Two’s Complement
Unsigned Integers
Signed Integers
Slide by Bohn
sign bit
Notes: The leading bit, the most significant bit, is the sign bit.
0 = non-negative
1 = negative
If the sign bit is 0, a given bit arrangement has the same value whether or not the integer is a signed integer or an unsigned integer.
If the sign bit is 1, then a given bit arrangement has a positive value if it is an unsigned integer, or a negative value if it is a signed integer.

## Slide 19: Bit-level representation, by type size
Type | Size | Binary | Hexadecimal
char | 8 bits | (insufficient bits) | 
short | 16 bits | 0000 0000 1110 0111 | 00 E7
int | 32 bits | 0000 0000 0000 0000 0000 0000 1110 0111 | 00 00 00 E7
long | 64 bits | 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 1110 0111 | 00 00 00 00 00 00 00 E7
Slide by Bohn
Representation of 23110
assuming 64-bit processor
Type | Size | Binary | Hexadecimal
char | 8 bits | (insufficient bits) | 
short | 16 bits | 1111 1111 1111 0101 | FF 19
int | 32 bits | 1111 1111 1111 1111 1111 1111 1111 0101 | FF FF FF 19
long | 64 bits | 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 1111 0101 | FF FF FF FF FF FF FF 19
Representation of -231
Notes: Notice that negative values aren’t simply the positive-value representation with a ‘1’ sign bit.
Notice that for non-negative values, as we add bits, the extra bits are 0;
For negative values, as we add bits, the extra bits are 1.
** Sign Extension **

## Slide 20: Maximum Values, by type size
Constant | Value
UCHAR_MIN | 0
UCHAR_MAX | 255
USHORT_MIN | 0
USHORT_MAX | 65,535
UINT_MIN | 0
UINT_MAX | 4,294,967,295U
ULONG_MIN | 0
ULONG_MAX | 18,446,744,073,709,551,615UL
Slide by Bohn
assuming 64-bit processor
Constant | Value
CHAR_MIN | -128
CHAR_MAX | 127
SHORT_MIN | -32,768
SHORT_MAX | 32,767
INT_MIN | -2,147,483,648
INT_MAX | 2,147,483,647
LONG_MIN | -9,223,372,036,854,775,808L
LONG_MAX | 9,223,372,036,854,775,807L

## Slide 21: Maximum Values, by type size – in hexadecimal
Constant | Value
UCHAR_MIN | 0x0
UCHAR_MAX | 0xFF
USHORT_MIN | 0x0
USHORT_MAX | 0xFF FF
UINT_MIN | 0x0
UINT_MAX | 0xFF FF FF FF U
ULONG_MIN | 0x0
ULONG_MAX | 0xFF FF FF FF FF FF FF FF UL
Slide by Bohn
assuming 64-bit processor
Constant | Value
CHAR_MIN | 0x80
CHAR_MAX | 0x7F
SHORT_MIN | 0x80 00
SHORT_MAX | 0x7F FF
INT_MIN | 0x80 00 00 00
INT_MAX | 0x7F FF FF FF
LONG_MIN | 0x80 00 00 00 00 00 00 00 L
LONG_MAX | 0x7F FF FF FF FF FF FF FF L

## Slide 22: Addition: Signed Integer Overflow
Slide by Bohn
Constant | Value
CHAR_MIN | 0x80
CHAR_MAX | 0x7F

## Slide 23: Where does overflow happen?
Slide by Bohn
8-bit
Unsigned
00..00
00..01
00..10
01..01
01..10
01..11
. . .
. . .
11..01
10..10
11..10
10..01
11..11
10..00
. . .
0
1
2
125
126
127
128
129
130
253
254
255
8-bit
Signed
(2’s comp)
00..00
00..01
00..10
01..01
01..10
01..11
. . .
. . .
11..01
10..10
11..10
10..01
11..11
10..00
. . .
0
1
2
125
126
127
-128
-127
-126
-3
-2
-1
Overflow happens here
greatest value
least value
greatest value
least value
. . .
. . .

## Slide 24: An easier way to find bits for negative value
Adding 1 to greatest non-negative value produces least negative value
  Modular arithmetic
Adding 1 to greatest negative value produces least non-negative value
  -1 + 1 = 0
What is two’s complement representation of -1?
Slide by Bohn
Notes: -1 + 1 = 0 isn’t particularly shocking.

## Slide 25: An easier way to find bits for negative value
Slide by Bohn
-1 = -TYPE_MIN + TYPE_MAX
Notes: b_{n-1} has to be a 1, because -1 is negative.
We already know that -2^{n-1}, which is TYPE_MIN, is 100…00.
The remaining summation is 1s in every position except the sign bit.
We already know that TYPE_MAX + 1 = TYPE_MIN, so it’s no surprise that -1 = -TYPE_MIN + TYPE_MAX
Adding those together, we get all ones…
… or all F’s

## Slide 26: An easier way to find bits for negative value
Slide by Bohn
Notes: Well this is interesting

## Slide 27: An easier way to find bits for negative value
Slide by Bohn

## Slide 28: Examples
Slide by Bohn

## Slide 29: Signed Addition
Slide by Bohn
assuming signed char
= 810

## Slide 30: Addition: Ripple-Carry Adder
Slide by Bohn
1-bit Full Adder
A0
B0
0
Sum0
1-bit Full Adder
A1
B1
Sum1
carry
carry
1-bit Full Adder
A2
B2
Sum2
1-bit Full Adder
A3
B3
Sum3
carry
carry
Notes: With two’s complement, we can use the same hardware for addition that we did for unsigned integers!

## Slide 31: Subtraction: Ripple-Carry Adder
Slide by Bohn
1-bit Full Adder
A0
~B0
1
Sum0
1-bit Full Adder
A1
~B1
Sum1
carry
carry
1-bit Full Adder
A2
~B2
Sum2
1-bit Full Adder
A3
~B3
Sum3
carry
carry
  Recall:
  -x == ~x + 1
A - B
= A + (-B)
= A + ~B + 1
Notes: Subtraction is really addition!

## Slide 32: Addition/Subtraction: Ripple-Carry Adder
Switch between addition & subtraction with a single bit
On subtract
  complement second operand
  pass 1 into carry-in
Slide by Bohn
1-bit Full Adder
A0
B0
Sum0
1-bit Full Adder
A1
B1
Sum1
carry
carry
0. 1
MUX
. . .
0. 1
MUX
0 = ADD
1 = SUBTRACT
Notes: With two’s complement, we can use the same hardware for addition that we did for unsigned integers!

## Slide 33: When does overflow happen?
UNSIGNED
A + B = C
  If C<A, overflow has occurred
  Umax-A < B
A – B = C
  If C>A, overflow has occurred
  A<B
    Equivalent to A-0 < B
SIGNED (2’s comp)
A + B = C A≥0, B≥0
  If C<A, overflow has occurred
  Tmax-A < B
A + B = C A≤0, B≤0
    Equivalent to A - B = C A≤0,B≥0
  If C>A, overflow has occurred
  A-Tmin< |B|
Slide by Bohn
SAME CONDITIONS
at the interpretation level
but different
at the bit level
Notes: Unsigned: if the sum is less than the addend or augend, then overflow must’ve happened
Signed: if the addend and augend have the same sign (+ or -) but the sum has the opposite sign (e.g., adding two positive values and getting a negative sum), then overflow must’ve happened

## Slide 34: Where does overflow happen?
Slide by Bohn
8-bit
Unsigned
00..00
00..01
00..10
01..01
01..10
01..11
. . .
. . .
11..01
10..10
11..10
10..01
11..11
10..00
. . .
0
1
2
125
126
127
128
129
130
253
254
255
8-bit
Signed
(2’s comp)
00..00
00..01
00..10
01..01
01..10
01..11
. . .
. . .
11..01
10..10
11..10
10..01
11..11
10..00
. . .
0
1
2
125
126
127
-128
-127
-126
-3
-2
-1
Overflow happens here
greatest value
least value
greatest value
least value

## Slide 35: When does overflow happen?
UNSIGNED
Is the MSB carry-out bit different from the LSB carry-in bit?
SIGNED (2’s comp)
When viewed as addition:
If both operands have same sign, does sum have the opposite sign?
Is the MSB carry-out bit different from the MSB carry-in bit?
Slide by Bohn

## Slide 36: Unsigned Addition/Subtraction Integer Overflow
Slide by Bohn
1-bit Full Adder
A0
B0
Cin_0
Sum0
1-bit Full Adder
A1
B1
Sum1
carry
carry
1-bit Full Adder
A2
B2
Sum2
1-bit Full Adder
A3
B3
Sum3
carry
carry
If Cout_n-1 ^ Cin_0 = 1 then unsigned addition/subtraction overflowed

## Slide 37: Signed Addition/Subtraction Integer Overflow
Slide by Bohn
1-bit Full Adder
A0
B0
Cin_0
Sum0
1-bit Full Adder
A1
B1
Sum1
carry
carry
1-bit Full Adder
A2
B2
Sum2
1-bit Full Adder
A3
B3
Sum3
carry
carry
If
An-1 = Bn-1 ≠ Sumn-1 then signed addition/subtraction overflowed
If Cin_n-1 ^ Cout_n-1 = 1 then signed addition/subtraction overflowed
Notes: Two different ways to detect overflow at the bit-level

## Slide 38: Casting Between Integer Types

## Slide 39: Casting between signed & unsigned integers
Keep bit representation unchanged; Reinterpret as signed/unsigned
MSB is 0 (0 ≤ value ≤ TYPE_MAX): value remains unchanged
MSB is 1 (value < 0 -or- TYPE_MAX < value ≤ UTYPE_MAX): value = value ± 2n value = value ± (UTYPE_MAX + 1)
Slide by Bohn
Bit Pattern | Unsigned Value | Signed Value
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
Large positive/negative weight

## Slide 40: Casting between signed & unsigned integers: Examples
short s = -53; printf("%d\n”, (unsigned short)s);
Output: 65483
Explanation: -53 = 0xFFCB (signed short) 0xFFCB = 65,483 (unsigned short)
unsigned u = 2461583105; printf("%d\n”, (int)u);
Output: -1833384191
Explanation: 2,461,583,105 = 0x92B8C701 (unsigned int) 0x92B8C701 = -1,833,384,191 (int)
Slide by Bohn

## Slide 41: Casting between signed & unsigned integers: Constants
By default, constants are signed integers
Unsigned constants must have ‘U’ suffix
  0U, 4294967295U
Casting during assignment can be explicit or implicit
  unsigned int foo = (unsigned int)-3;
  unsigned int bar = -5;
Slide by Bohn

## Slide 42: Casting between signed & unsigned integers: Explicit & Implicit Casting
Assignment
Can be explicit or implicit
Implicit casting of RHS to match LHS type
unsigned char foo = (unsigned char) -3;
  foo == 253
unsigned char bar = -5;
  bar == 251
Expression Evaluation
Arithmetic, comparison, etc.
If mixing signed & unsigned values, signed values implicitly cast to unsigned!
Sometimes surprising, sometimes not:
  -1 < 0 but -1 > 0U
  -1 > -2 and (unsigned)-1 > -2
Slide by Bohn

## Slide 43: Casting between different-sized types: Larger type to smaller type
Truncate, reinterpret remaining bits
(unsigned char)68588 = 236 0x00 01 0B EC truncates to 0xEC = 23610
(char)68588 = -20 0x00 01 0B EC truncates to 0xEC = -2010
Slide by Bohn
Notes: Might take this opportunity to convince ourselves that 0xEC = -20:
~0xEC + 1 = 0x13 + 1 = 0x14 = 20_{10}

## Slide 44: Casting between different-sized types: Smaller type to larger type
Unsigned: zero-extend value
  unsigned char a = 53; unsigned short s = a; // implicit casting
  a == 5310 == 0x35 s == 0x0035 == 5310
Signed: sign-extend value
  Duplicate original MSB into new bytes
Slide by Bohn

## Slide 45: Casting between different-sized types: Sign-Extension
 | Decimal | Hex | 
s | 25625 | 64 19 | 0110 0100 0001 1001
i | 25625 | 00 00 64 19 | 0000 0000 000 0000 0110 0100 0001 1001
t | -25625 | 9B E7 | 1001 1011 1110 0111
j | -25625 | FF FF 9B E7 | 1111 1111 1111 1111 1001 1011 1110 0111
Slide by Bohn
s
. . .
s
. . .
short s = 25625;
int i = (int)s;
short t = -25625;
int j = (int)t;
s
s
s
s
s
s
. . .
…
…

## Slide 46: Integer Multiplication & Division

## Slide 47: Multiplication
Multiply two n-bit integers
Potentially need 2n bits for product
Only have n bits available for product
Truncate high-order n bits
Implements modular arithmetic
Slide by Bohn
. . .
. . .
. . .
a
b
a•b
. . .

## Slide 48: Multiplication
In assembly code, it is possible to get high-order n bits in one result register and lower-order n bits in another result register
  Higher-order n bits for signed multiplication differ from unsigned multiplication
  Lower-order n bits are the same, regardless of signed or unsigned multiplication
Cannot access high-order n bits through C
  Unless you cast operands to larger type
Slide by Bohn

## Slide 49: Fast & Simple Multiplication
x * 2y = x * 100…00
x * 2y = x << y
Example: 2010 * 410 = 0001 01002 * 22 = 0101 00002 = 8010
If compiler knows either operand is power-of-2, it will substitute left-shift
  Shift is faster than multiply
Slide by Bohn
y 0’s

## Slide 50: Fast and Simple Multiplication: Use Distributive Property
Recall
Every integer can be expressed as sum of powers-of-two
Slide by Bohn
Notes: “Every integer can be expressed as sum of powers-of-two” – this is, after all, what the binary representation is!

## Slide 51: Fast and Simple Multiplication: Use Distributive Property
Two shifts & add are faster than multiplication
  If either operand is a constant, compiler may replace multiplication with shifts-and-add (or shifts-and-subtract)
  Diminishing returns limit opportunity for benefit
Examples
  j*40 == j*(32+8) == j*32 + j*8 == (j<<5)+(j<<3)
  j*56 == j*(64-8) == j*64 - j*8 == (j<<6)-(j<<3)
Slide by Bohn

## Slide 52: Division
Computationally expensive
Compiler will avoid dividing if it can
If divisor is constant power-of-two, can replace division with right-shift
More limited than left-shift for multiplication
  Multiplication works with either operand (due to commutativity); division only works with divisor
  Multiplication works with any constant (due to distributivity); division only works with exact powers-of-two
Slide by Bohn
Notes: “Compiler will avoid dividing if it can”
From lab 5, this line
reduced_character = (reduced_character + key + 26) % 26;
Compiles to
# the next 8 lines are the compiler bending over backwards to avoid dividing
imulq $1321528399, %rax, %r10 ## imm = 0x4EC4EC4F
movq %r10, %r9 # x = reduced_character * <number>
shrq $63, %r9 # sign = x's sign bit
shrq $35, %r10 # x = upper 29 bits of x
addl %r9d, %r10d # x = x + sign
leal (%r10,%r10,4), %ecx
leal (%rcx,%rcx,4), %ecx
addl %r10d, %ecx # c = 26 * x
subl %ecx, %eax # reduced_character -= c

## Slide 53: Fast & Simple Division: Unsigned Integers
Uses logical right-shift
Always produces correct quotient
Slide by Bohn

## Slide 54: Fast & Simple Division: Signed Integers
Uses arithmetic right-shift
Rounds in wrong direction if x < 0
Error corrected by introducing a bias:
Slide by Bohn