## Slide 1: Representing Data
Programming at the Hardware/Software Interface

## Slide 2
You are free to:
Share — copy and redistribute the material in any medium or format
Adapt — remix, transform, and build upon the material for any purpose, even commercially
Under the following terms:
Attribution — You must give appropriate credit, provide a link to the license, and indicate if changes were made. You may do so in any reasonable manner, but not in any way that suggests the licensor endorses you or your use.
No additional restrictions — You may not apply legal terms or technological measures that legally restrict others from doing anything the license permits.
Slide by Bohn
This work is licensed under a Creative Commons Attribution 4.0 International License. This work is ©2018-21 Christopher A. Bohn, bohn@unl.edu.
These lecture slides are meant to enhance your use of the Programming at the Hardware/Software Interface textbook. If you have not adopted this publication for your course, please consider doing so.

## Slide 3: Number Bases

## Slide 4: Choosing a number base
What number base is obvious? Why?
Slide by Bohn
Notes: Most students will probably answer base 2, but that’s really a hindsight-driven statement. Nonetheless, go with it: what is “obvious” about binary numbers?
But even if they answer base 10, have them explain why that’s obvious.
And if they answer something else, I’m sure there’ll be a good discussion.

## Slide 5: Choosing a number base
Base 10: 0 1 2 3 4 5 6 7 8 9
  Human “standard” number base – probably because we have 10 fingers
    Digit (noun): a finger or toe
    Digit (noun): a numeral when used to form part of a number
Slide by Bohn

## Slide 6: Choosing a number base
Base 10 [0 1 2 3 4 5 6 7 8 9]
  Human-standard number base
  Digit = Finger
  Digit = each numeral in a number representation
  Even carries through in scientific notation
    6.8588 X 104
Implementing Electronically
  Hard to store
    ENIAC (First electronic computer) used 10 vacuum tubes / digit
  Hard to transmit
    Need high precision to encode 10 signal levels on single wire
  Messy to implement digital logic functions
    Addition, multiplication, etc.
Slide by Bohn

## Slide 7: Choosing a number base
Base 2 [0 1]
  “Binary Digit”
Easy to store
  Punch cards / punch tape
  Position of switch
  Voltage amplitude
  Transmission: Binary Frequency Shift Keying
Downside
  Not human-readable
GCC allows binary representation with “0b”
  100111012 can be written as 0b10011101 (becomes unwieldy with more bits)
Slide by Bohn
FSK of “Hello World,” prepared by Bohn
Punch card / punch tape ©Shutterstock.com
Vacuum tube / transistor photo by Bohn

## Slide 8: Choosing a number base
Binary Coded Decimal (BCD)
Uses four bits to represent decimal values
  Easy conversion to human-readable form
  Wiring processors to perform math just as convoluted as ENIAC
Slide by Bohn

## Slide 9: Choosing a number base
Base 16 [0 1 2 3 4 5 6 7 8 9 A B C D E F]
Hexadecimal, or “hex”
A more-compact representation of Base 2
  (Slightly) more human-readable than binary
  Each hex digit corresponds to four bits
  Exactly two hex digits needed to represent a byte
In C, indicate hex representation with “0x”
  FA1D37B16 would be written 0xFA1D37B (or 0xfa1d37b)
Slide by Bohn
Hex | Binary | Decimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
A | 1010 | 10
B | 1011 | 11
C | 1100 | 12
D | 1101 | 13
E | 1110 | 14
F | 1111 | 15

## Slide 10: Radix Conversions: Binary to Hex, Hex to Binary
Hexadecimal to Binary
  Replace hex-digit with corresponding four bits
Binary to Hexadecimal
  Separate bits into quartets starting with LSB
  Replace each quartet with corresponding hex-digit
Slide by Bohn
Hex | Binary | Decimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
A | 1010 | 10
B | 1011 | 11
C | 1100 | 12
D | 1101 | 13
E | 1110 | 14
F | 1111 | 15

## Slide 11: Radix Conversions: Binary to Decimal
Apply weighted sums
  “Ones” place adds 0 or 1
  “Twos” place adds 0 or 2
  “Fours” place adds 0 or 4
  “Eights” place adds 0 or 8
  …
  2is place adds 0 or 2i
Slide by Bohn
Hex | Binary | Decimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
A | 1010 | 10
B | 1011 | 11
C | 1100 | 12
D | 1101 | 13
E | 1110 | 14
F | 1111 | 15

## Slide 12: Radix Conversions: Decimal to Binary (repeated division)
Repeatedly divide by 2
  Remainder of each division becomes a bit
  Stop when quotient is 0
Slide by Bohn
Hex | Binary | Decimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
A | 1010 | 10
B | 1011 | 11
C | 1100 | 12
D | 1101 | 13
E | 1110 | 14
F | 1111 | 15
1
1
0
1
0
0
1
0

## Slide 13: Radix Conversions: Decimal to Binary (repeated subtraction)
Repeatedly subtract by powers-of-two
  Start with greatest power-of-two less than value
  If power-of-two is less than working value, subtract, place a 1 bit, and go to next-smaller power-of-two
  Otherwise, place a 0 bit and go to next-smaller power-of-two
Slide by Bohn
Hex | Binary | Decimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
A | 1010 | 10
B | 1011 | 11
C | 1100 | 12
D | 1101 | 13
E | 1110 | 14
F | 1111 | 15
1
1
0
1
0
0
1
0

## Slide 14: Radix Conversions: Decimal to Hex, Hex to Decimal
Treat as chained conversion between decimal & binary and binary & hexadecimal
Slide by Bohn
Hex | Binary | Decimal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 8
9 | 1001 | 9
A | 1010 | 10
B | 1011 | 11
C | 1100 | 12
D | 1101 | 13
E | 1110 | 14
F | 1111 | 15

## Slide 15: From Bits to Bytes

## Slide 16: Byte
8 bits
Binary: 0b00000000 to 0b11111111
Hexadecimal: 0x00 to 0xFF
As integer, 010 to 25510 or -12810 to 12710
As character
  128 ASCII characters plus 128 non-standard “Extended ASCII” characters, or
  the first 128 UTF-8 characters (with most-significant bit fixed as 0)
Slide by Bohn

## Slide 17: Hexdump nonTerminatingLoop.c source file
Slide by Bohn
Screenshot showing byte-level representation of plain-text file
Notes: Note that each byte uses 2 hex digits (because each hex digit represents 4 bits)

## Slide 18: Word
“Word size”
  Size of data representations inside processor
  Often nominal size of integer, memory address
Older machines
  8-bit (1 byte) – Z80, 6502
  16-bit (2 byte) – 8086, 68000
  32-bit (4 byte) – Pentium, PowerPC
Typical modern microprocessor – 64-bit (8 byte)
Data types may be 1 word, multiple words, or a fraction of a word
  (almost) Always an exact-integer number of bytes
Slide by Bohn
Notes: Notable exception to “always an exact-integer”: Five 7-bit characters fit in 36-bit word of now-obsolete scientific computers
Notable exception to common assumption that data types are powers-of-two in size: x87’s 10-byte non-754-compliant FP type

## Slide 19: Sizes of Data Types
C data type | 8-bit processor | 16-bit processor | 32-bit processor | 64-bit processor
char | 1 | 1 | 1 | 1
short | 2 | 2 | 2 | 2
int | 2 | 2 | 4 | 4
long | 4 | 4 | 4 | 8
long long | 8 | 8 | 8 | 8
float | 4 | 4 | 4 | 4
double | 4 | 8 | 8 | 8
long double | 4 | 8+ (10 on IA16) | 8-16 (10/12 on IA32) | 8-16 (10/16 on x86-64)
pointer | 2 | 2 | 4 | 8
Slide by Bohn
Unsure?
Use C’s sizeof() operator
Want a guaranteed size?
Use int8_t, uint8_t, int16_t, uint16_t, etc.
Notes: Not too many 16-bit CPUs in use today.
MPUs tend to be 64 bit (e.g., modern Intel & AMD x86, ARM Cortex-A in Raspberry Pi 3-4, Apple M1), occasionally 32 bit (e.g., ARM Cortex-A in Raspberry Pi 1-2 & Terasic Altera DE10, Altera Nios II FPGA-based processor)
MCUs tend to be 8 bit (e.g., ATK in most Arduinos) or 32 bit (ARM Cortex-M in Arduino Due or Raspberry Pi Pico)
x86 long double is a 10-byte FP type that pre-dates FP standard (chap4) and doesn’t comply with it. For performance reasons (chap6), it gets padded-out to 12 bytes on IA32 and 16 bytes on x86-64.
uint8_t, etc, are defined in stdint.h, introduced in 1999 C standard. Rarely used except as bit vectors.

## Slide 20: Multi-byte Values in Memory: Addresses
Address specifies byte in memory
Multi-byte value’s address is the lowest address
Subsequent values’ addresses differ by
  2 (16 bit type)
  4 (32 bit type)
  8 (64 bit type)
Slide by Bohn
Address
0x103F
0x103E
0x103D
0x103C
0x103B
0x103A
0x1039
0x1038
0x1037
0x1036
0x1035
0x1034
0x1033
0x1032
0x1031
0x1030
1-byte values
Addr= 0x103E
Addr= 0x103C
Addr= 0x103A
Addr= 0x1038
Addr= 0x1036
Addr= 0x1034
Addr= 0x1032
Addr= 0x1030
2-byte values
Addr= 0x103C
Addr= 0x1038
Addr= 0x1034
Addr= 0x1030
4-byte values
Addr= 0x1038
Addr= 0x1030
8-byte values

## Slide 21: Multi-byte Values in Memory: Byte Ordering
Big Endian
Least significant byte has highest address
68k, PowerPC, SPARC, Internet, Java
Little Endian
Least significant byte has lowest address
x86, ARM, Alpha, RISC-V
Slide by Bohn
Address
0x1039
0x1038
0x1037
0x1036
0x1035
0x1034
0x1033
0x1032
67
56
34
12
Big
Endian
12
34
56
78
Little
Endian
Example
4-byte integer
i == 0x12345678
&i == 0x1034
Unsure?
Use GCC’s __BYTE_ORDER__ pre-defined macro
Notes: Strictly speaking, ARM is “bi-endian,” but it defaults to little endian.
Opportunity to point out value of using hexadecimal. In binary,
i = 0b00010010001101000101011001111000
Opportunity to remind students that &i creates a pointer to i. A pointer is a variable that contains a memory address – in this case, it contains the address of i. The pointer points to i.

## Slide 22: Multi-byte Values in Memory: Testing for Endianness
Intel Core i7
Java
Slide by Bohn
Screenshot of output from endian_test.c
Screenshot of output from EndianTest.java
Notes: On left: LSB (0xEF) is at lowest address (0x7FFEE05B28E0)
On right: LSB is in the higher-order byte
Consider doing this as a live demo

## Slide 23: Multi-byte Values in Memory: Byte-Reversed Listings
Disassembly
  Reconstructs plain-text assembly code from binary object code
  Example: objdump -d endian_test
Snippet: Address Machine Code Assembly Code 100000d8f: 89 d6 movl %edx, %esi 100000d91: 81 ee d2 04 00 00 subl $1234, %esi 100000d97: 89 45 bc movl %eax, -68(%rbp)
Slide by Bohn
Value 123410 = 0x4D2
Pad to 4 bytes 0x4D2 = 0x 00 00 04 D2
Appears reversed due to little-endianness

## Slide 24: Pointers: Variables that hold memory addresses
Big
Endian
Little
Endian
int *p; *p = 147456;
147456 = 217 + 214
= 0000 0000 0000 0010 0100 0000 0000 00002
= 0x00024000
Slide by Bohn
Address
0x1039
0x1038
0x1037
0x1036
0x1035
0x1034
0x1033
0x1032
0x1034
p
👉
00
40
02
00
00
02
40
00
Equivalently:
int i = 147456;
int *p = &i;

## Slide 25: Pointers: An Analogy
Slide by Bohn
12344
12345
12346
12345 Sesame Street
The envelope does not contain the house
The envelope contains the address of the house
12345 Sesame Street
Multiple envelopes can contain the same address
12346 Sesame Street
Changing one envelope’s address does not affect other envelopes
If the house changes, people holding each envelope see the change

## Slide 26: C Strings
Array of ASCII characters
Terminated with ASCII NUL
  '\0’
  0x00
Byte ordering not relevant
  A string is not a multibyte type
  A string is an array of 1-byte char
  A string is a pointer to a char
Slide by Bohn
char s[] = "68588";
00
38
38
35
38
36
Big
Endian
00
38
38
35
38
36
Little
Endian
Address
0x103A
0x1039
0x1038
0x1037
0x1036
0x1035
0x1034
0x1033
0x1034
s
👉
Notes: See ASCII table for ASCII character mappings

## Slide 27: Machine-Level Code Representation
Programs are byte sequences
Encode Program as Sequence of Instructions
  Each instruction is a simple operation
    Arithmetic operation
    Read or write memory
    Conditional branch
  Instructions encoded as bytes
    Different instruction set architectures interpret bytes differently
    ARM, PowerPC (pre-2006 Mac) use 4 byte instructions
      Reduced Instruction Set Computer (RISC)
    x86 uses variable length instructions
      Complex Instruction Set Computer (CISC)
Slide by Bohn

## Slide 28: Hexdump loopIndexing executable file
Slide by Bohn

## Slide 29: Instruction Set Architectures: Different Bytes for same C-level code
int add(int x, int y) { return x+y; }
Compile with gcc -Og …
  x86 uses a 3-byte instruction and a 1-byte instruction
  ARM uses two 4-byte instructions
X86-64 401136: 8d 04 37 lea (%rdi,%rsi,1),%eax 401139: c3 ret
ARM64 400620: 0b 01 00 00 add w0, w0, w1 400624: d6 5f 03 c0 ret
Slide by Bohn

## Slide 30: Bit Operations

## Slide 31: Bit Operations: Logical Operators vs Bitwise Operators
Logical Operators
Operands are any integer type
False = 0
True = non-zero (operators return 1 for True)
AND a && b
OR a || b
NOT !a
Bitwise Operators
Operators are any integer type
Treats operators as bit vectors
Applies operation to each bit position
AND a & b
OR a | b
NOT ~a
XOR a ^ b
Slide by Bohn
Notes: My students take discrete math course before this course. If yours haven’t, you may want to cover these operators – though the logical operators should’ve also been covered in CS1.

## Slide 32: Boolean and Integer Algebras
Integer
Addition (+) is the “sum” operation
Multiplication (*) is the “product” op
Subtraction (-) is the additive inverse
0 is the identity for sum (x+0=x)
1 is the identity for product (x*1=x)
Boolean
Or (|) is the “sum” operation
And (&) is the “product” operation
Not (~) is the “complement” operation
  Not additive inverse
0 is the identity for sum (x|0=x)
1 is the identity for product (x&1=x)
Slide by Bohn

## Slide 33: Boolean and Integer Algebras – similarities
Integer
Commutativity
  A+B = B+A
  A*B = B*A
Associativity
  (A+B)+C = A+(B+C)
  (A*B)*C = A*(B*C)
Product distributes over sum
  A*(B+C) = A*B + A*C
Sum and product identities
  A+0 = A A*1 = A
Zero is product annihilator
  A*0 = 0
Cancellation of negation
  -(-A) = A
Boolean
Commutativity
  A|B = B|A
  A&B = B&A
Associativity
  (A|B)|C = A|(B|C)
  (A&B)&C = A&(B&C)
Product distributes over sum
  A&(B|C) = A&B | A&C
Sum and product identities
  A|0 = A A&1 = A
Zero is product annihilator
  A&0 = 0
Cancellation of negation
  ~(~A) = A
Slide by Bohn

## Slide 34: Boolean and Integer Algebras – differences
Integer
Sum doesn’t distribute over product
  A+(B*C) ≠ (A+B) * (A+C)
No idempotency
  A+A ≠ A
No absorption
  A+(A*B) ≠ A
  A*(A+B) ≠ A
Additive Inverse
  A+ -A =0
No Law of Complements
Boolean
Sum distributes over product
  A|(B&C) = (A|B) & (A|C)
Idempotency
  A|A = A
  A&A = A
Absorption
  A|(A&B) = A
  A&(A|B) = A
Laws of Complements
  A|~A =1
  A&~A = 0
No additive inverse
Slide by Bohn

## Slide 35: Boolean Algebra – derived operators
XOR (“exclusive or”)
  A^B is 1 if only A is 1, or if only B is 1
  A^B is 0 if both A and B are 1 or if, or if both are 0
  A^B = A&~B | ~A&B
  A^A = 0 A^~A = 1
  A^0 = A A^1 = ~A
NAND, NOR, XNOR
  “Not AND,” “Not OR,” “Not XOR”
  Not used in C, found in logic gates
Slide by Bohn

## Slide 36: Bit Operations: Bitwise Boolean Operators
Slide by Bohn
0101 1010
& 1100 0011
0101 1010
| 1100 0011
0101 1010
^ 1100 0011
~ 1100 0011
0100 0010
1101 1011
1001 1001
0011 1100
uint8_t i = 0x37;
uint8_t j = 0x6C;
uint16_t k = 0x6C;
i & j ==
0011 0111
& 0110 1100
0010 0100
0x24
i | j ==
| 0110 1100
0111 1111
^ 0110 1100
0101 1011
~ 0110 1100
1001 0011
0x7F
i ^ j ==
0x5B
~j ==
0x93
~k ==
0xFF93
~ 0000 0000 0110 1100
1111 1111 1001 0011

## Slide 37: Bit Operations: Bit Shift Operators
Left Shift x << y
  Move x’s bits to the left by y positions
  Fill with 0s on right
  Truncate excess bits on left
Right Shift x >> y
  Move x’s bits to the right by y positions
  Truncate excess bits on right
  Logical shift: fill with 0s on left
  Arithmetic shift: duplicate leftmost bit
Slide by Bohn
01011010000
0x5A << 3
0x5A << 3 = 0xD0
00001011010
0x5A >> 3
0x5A >> 3 = 0x0D
00001011010
0x5Au >> 3
0x5Au >> 3 = 0x0Du
10100101000
0xA5 << 2
0xA5 << 2 = 0x94
11110100101
0xA5 >> 2
0xA5 >> 2 = 0xE9
00010100101
0xA5u >> 2
0xA5u >> 2 = 0x29u

## Slide 38: Bitmasks: Setting/Clearing a Bit
Slide by Bohn
XXXX XXXX
& 0000 0000
0000 0000
Clear every bit
XXXX XXXX
& 1111 1011
XXXX X0XX
Clear bit2
XXXX XXXX
| 1111 1111
1111 1111
Set every bit
XXXX XXXX
| 0010 0000
XX1X XXXX
Set bit5
foo & 0x4
foo & 0x20
~ XXXX XXXX
YYYY YYYY
Negate every bit
XXXX XXXX
^ 0100 0000
XYXX XXXX
Negate bit 6
foo ^ 0x40
Notes: Bitmasks take advantage of Boolean dominance & absorption

## Slide 39: Bitmasks: Testing a Bit
Slide by Bohn
XXXX XXXX
& 0000 0100
if (foo & 0x4)
Is bit2 a 1?
~ XXXX XXXX
& 0010 0000
if (~foo & 0x20)
Is bit5 a 0?
if !(foo & 0x20)
Notes: Even though (~foo & 0x20) and !(foo & 0x20) produce different values when bit5 is a 0, they are logically equivalent.

## Slide 40: Bitmasks: Parametric Bitmasks
Slide by Bohn
All 0s except 1 at bit y
0x1 << y
All 1s except 0 at bit y
~(0x1 << y)
All 0s except 1s at bits y & z
(0x1 << y) | (0x1 << z)
All 1s except 0s at bits y & z
~((0x1 << y) | (0x1 << z))
~(0x1 << y) & ~(0x1 << z)
Notes: Last example makes use of DeMorgan’s Law

## Slide 41: Key Ideas
Hexadecimal as shorthand for binary
Radix conversions: hexadecimal  binary  decimal
It’s all bits & bytes – interpret differently for different uses
  Text, integer, address, machine code
Same uses can be different between machines
  Word size, endianness, instruction set architecture
Bit operations
  Bitwise AND, OR, XOR
  Left-shift, Logical & Arithmetic Right-shift
Bitmasks
Slide by Bohn