## Slide 1: Arithmetic for Binary Computers (ABCs) Floating Point Numbers
Programming at the Hardware/Software Interface

## Slide 2
You are free to:
Share — copy and redistribute the material in any medium or format
Adapt — remix, transform, and build upon the material for any purpose, even commercially
Under the following terms:
Attribution — You must give appropriate credit, provide a link to the license, and indicate if changes were made. You may do so in any reasonable manner, but not in any way that suggests the licensor endorses you or your use.
No additional restrictions — You may not apply legal terms or technological measures that legally restrict others from doing anything the license permits.
Slide by Bohn
This work is licensed under a Creative Commons Attribution 4.0 International License. This work is ©2018-21 Christopher A. Bohn, bohn@unl.edu.
These lecture slides are meant to enhance your use of the Programming at the Hardware/Software Interface textbook. If you have not adopted this publication for your course, please consider doing so.

## Slide 3: Fixed Point Binary Numbers

## Slide 4: Recall Integer Encoding
Slide by Bohn
bj
bj-1
. . .
b2
b1
b0
bits
weight
2j
2j-1
. . .
4
2
1

## Slide 5: Fixed Point Numbers: Encoding
Slide by Bohn
bj
bj-1
. . .
b2
b1
b0
bits
weight
2j
2j-1
. . .
4
2
1
b-1
b-2
b-3
. . .
b-k+1
b-k
½
¼
⅛
. . .
2-k+1
2-k
Binary point
integer portion
fractional portion

## Slide 6: Fixed Point Numbers: Examples
Integers are special-case of fixed-point values
Divide by 2 by shifting right
Multiply by 2 by shifting left
0.0000…12 = ε is least value greater than 0.0
0.11111…2 = 1-ε is greatest value less than 1.0
Value Encoding
18210 101101102
9110 10110112
46½10 101101.12
22¾10 10110.112
11⅜10 1011.0112
511/1610 101.10112
227/3210 10.110112
127/6410 1.0110112
91/12810 0.10110112
Slide by Bohn

## Slide 7: Fixed Point Numbers: Not difficult to read
Slide by Bohn
bj
bj-1
. . .
b2
b1
b0
bits
weight
2j
2j-1
. . .
4
2
1
b-1
b-2
b-3
. . .
b-k+1
b-k
½
¼
⅛
. . .
2-k+1
2-k
integer portion
fractional portion
Example: 1011.1012 = 11⅝10
Notes: 1011_2 = 11_{10}
101_2 = 5_{10}
2^3 = 8

## Slide 8: Fixed Point Numbers: Limitations
Cannot exactly represent all fractions
  Exactly represents only numbers of the form n/2k
  Other rational numbers have repeating bit representations
1/310 = 0.0101[01]…2
1/510 = 0.00110011[0011]…2
1/1010 = 0.0001100110011[0011]…2
Slide by Bohn
Notes: Both this slide and the next slide: the limitation is that there are a finite number of bits
Decimal fractions have the same problem, except the problem is with fractions not of the form n/10k

## Slide 9: Fixed Point Numbers: Limitations
Cannot represent both large and small values
Given n bits total
  More bits for integer portion (for large values) leaves fewer bits for fractional portion
  More bits for fractional portion (for small values) leaves fewer bits for integer portion
We can fix this problem with floating point numbers
Slide by Bohn
Notes: Both this slide and the previous slide: the limitation is that there are a finite number of bits

## Slide 10: Digression: Decimal Fixed Point Value Hack
Notes: But first…

## Slide 11: Why Fixed Point Decimal?
Floating point numbers solve the large/small problem
Floating point numbers do not solve the limits on representable fractions
Inability to represent 0.01 problematic for decimal currency
Slide by Bohn

## Slide 12: Decimal Fixed Point Hack
Slide by Bohn
https://www.wsj.com/articles/berkshire-hathaways-stock-price-is-too-much-for-computers-11620168548
https://www.military.com/daily-news/2019/12/05/thousands-tricare-patients-billed-100-times-more-premium-glitch.html
If unit is a tenth/hundredth/thousandth/ten-thousandth/etc., then store as integer and use software to insert decimal point
Can introduce pernicious bug
Does not solve large/small problem

## Slide 13: Floating Point Binary Numbers
Format

## Slide 14: Floating Point Numbers: Nothing New
Floating point: the radix-point “floats” among the significand’s digits; its position is defined by an exponential factor
Normalized floating point: the integer portion of the significand consists of exactly one non-zero digit
“Scientific Notation” is normalized floating point
Slide by Bohn

## Slide 15: Floating Point Numbers: Nothing New
Floating point: the radix-point “floats” among the significand’s digits; its position is defined by an exponential factor
Normalized floating point: the integer portion of the significand consists of exactly one non-zero digit
“Scientific Notation” is normalized floating point
Slide by Bohn

## Slide 16: IEEE Standard 754: Overview
Uniform standard for floating point arithmetic
  Established in 1985, updated in 2008 & 2019
  Before standard, many formats used
Supported by all major CPUs
Numerical properties more important than computational speed
  Graceful overflow, underflow
  Well-defined rounding
Can re-use integer comparators
  0.0 has same encoding as 0
  MSB is sign bit
  If af < bf then same bits interpreted as integers implies ai < bi
Slide by Bohn

## Slide 17: IEEE Standard 754: Representation
Slide by Bohn
S
E
T
significand
fractional portion of significand
exponent
encoding of exponent (not the exponent)
encoding of significand (not the significand)
sign bit
fractional portion of significand
Notes: This is the terminology from IEEE 754, just fine for written discussion where you can see the difference between ‘E’ and ‘e’ and don’t have to worry about confusing the sound of ‘E’ and ‘T’.
In the textbook I used the terminology from the standard.

## Slide 18: IEEE Standard 754: Representation
Slide by Bohn
S
E
fraction
Notes: This is terminology is more suitable for verbal discussion.
Notice that (for normalized numbers), the integer portion of the significand can only be 1. That means we don’t need to encode that 1 in the representation; it’s implicit.

## Slide 19: IEEE Standard 754: Precision Options
binary16 informally, “half precision”
binary32 “single precision” in IEEE 754-1985 float in C
binary64 “double precision” in IEEE 754-1985 double in C
binary128 informally, “quad precision” sometimes long double in C
Slide by Bohn
S
E
fraction
S
E
fraction
S
E
fraction
S
E
fraction
1 bit
5 bits
10 bits
1 bit
8 bits
23 bits
1 bit
11 bits
52 bits
1 bit
15 bits
112 bits
Notes: Most people use “half/single/double/quad precision” instead of “binary16/32/64/128”
16- and 128-bit precision were not in original standard
2008 standard also defines bit fields for 128+32n-bit precision
2008 standard also defines decimal types for these levels of precision (“decimal16/32/64/128”)
long double is not guaranteed to be binary128; for example, on x86-64, long double is x87’s 80-bit “extended precision”. On some other processors, long double is binary64.

## Slide 20: Intel x87 80-bit extended precision
Slide by Bohn
S
E
fraction
1 bit
15 bits
63 bits
1
(normal form)
S
E
fraction
1 bit
15 bits
62 bits
bits63..62
(other forms)
Notes: Encodings for zero/subnormal may have a 0 or 1 in bit63.
Encodings for infinity/NaN may have 00/01/10/11 in bits63..62.
80-bit extended precision is allowed by IEEE754, but it doesn’t fit the format of 3 well-defined fields

## Slide 21: Normal Numbers
E ∉ {000…00, 111…11} 000…01 ≤ E ≤ 111…10
Significand’s leading digit is implicitly 1 m = 1.fraction
  Doesn’t appear in bitfield – get a “free” bit of precision
  m = 1.0 when fraction=000..00
  m = 2.0 - ε when fraction=111…11
Exponent encoded as biased integer: exponent = E – bias
  bias = 2w-1 - 1, where w is number of exponent bits
Slide by Bohn
S
E
fraction

## Slide 22: Normal Numbers: Bias Examples
Exponent encoded as biased integer: exponent = E – bias
  bias = 2w-1 - 1, where w is number of exponent bits
Single precision
  w = 8
  bias = 27 - 1 = 127 1 ≤ E ≤ 254 -126 ≤ exponent ≤ 127
Double precision
  w = 11
  bias = 210 - 1 = 1023 1 ≤ E ≤ 2046 -1022 ≤ exponent ≤ 2023
Slide by Bohn
S
E
fraction

## Slide 23: Normal Numbers: Encoding Summary
Slide by Bohn
S
E
fraction
w bits
1 bit
n-w-1 bits
S=0 – positive
S=1 – negative
significand m = 1.fraction
fraction = xx…x2, the fractional portion of m
exponent = E - bias
E = exponent + bias
bias = 2w-1 - 1

## Slide 24: Normal Numbers: Encoding Example
float f = 68588.0;
Value 6858810 = 1 0000 1011 1110 11002 = 1.0000 1011 1110 1100 x 216
Significand m = 1.0000 1011 1110 1100 fraction = 0000 1011 1110 1100 0000 000
Exponent exponent = 1610 bias = 12710 E = 14310 = 1000 11112
Sign S = 0
Slide by Bohn
S
E
fraction
0
10001111
00001011111011000000000

## Slide 25: Normal Numbers: Decoding Example
double d = …;
1011111111101100111000000000000000000000000000000000000000000000
Significand m = 1.1100 1110 0000…
Exponent E = 011 1111 11102 = 102210 bias = 102310 exponent = -110
Sign S = 1 (negative)
Value -1.1100111 x 2-1 = -0.111001112 = -231 ÷ 28 = -231/256 = -0.90234375
Slide by Bohn
S
E
fraction

## Slide 26: Integer Representation vs Floating Point Representation
 | 6858810 | -23110 256
32-bit int | 0x00 01 0B EC | 0x00 00 00 00
64-bit long | 0x00 00 00 00 00 01 0B EC | 0x00 00 00 00 00 00 00 00
32-bit float | 0x47 85 F6 00 | 0xBF 67 00 00
64-bit double | 0xC0 F0 BE C0 00 00 00 00 | 0xBF EC E0 00 00 00 00 00
Slide by Bohn
0
100 0111 1
000 0101 1111 0110 0000 0000
1
011 1111 1110
1100 1110 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000
float f = 68588.0;
double d = -231.0/256;

## Slide 27: Integer Casting vs Floating Point Casting
Smaller integer type cast to larger integer type
  Zero/Sign-extend
Larger integer type cast to smaller integer type
  Truncate and re-interpret
Integer type to floating point type, or Floating point type to integer type
  Generate new bit pattern
  May not be exact
Smaller floating point type cast to larger floating point type
  Generate new bit pattern
Larger floating point type cast to smaller floating point type
  Generate new bit pattern
  May require rounding
Slide by Bohn
Notes: FP -> int may not even be correct due to overflow
double -> float might even round to 0 or to infinity

## Slide 28: Quarter Precision Floating Point
8-bit floating point type
Not a real IEEE 754 format
Same general form as IEEE 754 format
  MSB is sign bit
  Next four bits encode the exponent
  Remaining three bits encode the significand, bias=7
  Normal, subnormal, zero, NaN, Infinity
Slide by Bohn
S
E
fraction
1 bit
4 bits
3 bits
bias = 2w-1-1
= 23-1
Notes: Too small to be practical for actual use
Good size for hand-examples

## Slide 29: Quarter Precision: Encoding Example
quarter q = 3.25;
Value 3.2510 = 11.012 = 1.101 x 21
Significand m = 1.101 fraction = 101
Exponent exponent = 110 bias = 710 E = 810 = 10002
Sign S = 0
Slide by Bohn
S
E
fraction
0
1000
101
0x45

## Slide 30: Subnormal Numbers
Values too low for normal numbers
  aka denormal numbers
E = 000…00 fraction ≠ 000…00
Significand’s leading digit is implicitly 0 m = 0.fraction
Exponent: exponent = 1 – bias
Tradeoff precision for ability to represent values closer to 0
  Less-and-less precision as values get closer-and-closer to 0
Slide by Bohn
S
E = 0
fraction
Notes: IEEE 754-1985 called these denormal numbers; IEEE 754-2008 calls these subnormal numbers. Some people still use denormal.
E = 0x0 flags that a number is subnormal (or zero)
Implicit leading digit is 0, not 1
exponent = 1 - bias (note that E-bias is 0-bias) – essentially, exponent is the least “normal” exponent

## Slide 31: Zero Numbers
Values too low for subnormal numbers
  Mathematically does not have to be exactly 0
E = 000…00 fraction = 000…00
Two zero values: ±0
Slide by Bohn
S
E = 0
fraction = 0
Notes: Technically, zero is not subnormal, but I don’t think that there are adverse consequences if you think of it as subnormal – essentially, it’s a subnormal value that traded off its last bit of precision – it’s ±0.00..0 x 2^{1-bias}
±0 because it may not be exactly 0; it may be a limit approaching 0, and mathematically you want to know which side of 0 the limit is on.

## Slide 32: Special Values
Infinity
±∞
Value too great for normal numbers
E = 111…11
fraction = 000..00
NaN
Not-a-Number
No numeric value can be determined
E = 111…11
fraction ≠ 000..00
Slide by Bohn
S
E = 111…11
fraction
Notes: Notice that infinity is the next increment up from the greatest normal number (0 111…10 111 -> 0 111…11 000)
Unlike 0 being equallly interpretable as subnormal or as a special case, infinity cannot reasonably be interpreted as a normal number

## Slide 33: Floating Point Number Line
Slide by Bohn
S
E
fraction
-0
+0
-subnormal
+subnormal
-normal
+normal
-∞
+∞
NaN
Greatest non-infinite magnitude limited by #bits for exp
Least non-zero magnitude limited by #bits for frac
Precision limited by #bits for frac
Reduced precision as value approaches zero

## Slide 34: Quarter Precision: Dynamic Range (positive values only)
Slide by Bohn
 | S E fraction | exponent | Value | 
Zero | 0 0000 000 | -6 | 0 | 
Subnormal Numbers | 0 0000 001 | -6 | 0 1/8 x 2-6 = 1/512 | least non-zero number
 | 0 0000 010 | -6 | 0 2/8 x 2-6 = 2/256 | 
 | … … … … … … … |  |  | 
 | 0 0000 110 | -6 | 0 6/8 x 2-6 = 6/512 | 
 | 0 0000 111 | -6 | 0 7/8 x 2-6 = 7/512 | greatest subnormal number
Normal Numbers | 0 0001 000 | -6 | 1 0/8 x 2-6 = 8/512 | least normal number
Normal Numbers | 0 0001 001 | -6 | 1 0/8 x 2-6 = 9/512 | 
 | … … … … … … … |  |  | 
 | 0 0110 110 | -1 | 1 6/8 x 2-1 = 14/16 | 
 | 0 0111 111 | -1 | 1 7/8 x 2-1 = 15/16 | 1 - ε
 | 0 1000 000 | 0 | 1 0/8 x 20 = 1 | 
 | 0 1000 001 | 0 | 1 1/8 x 20 = 1 1/8 | 1 + ε
 | 0 1000 010 | 0 | 1 2/8 x 20 = 1 2/8 | 
 | … … … … … … … |  |  | 
 | 0 1110 110 | 7 | 1 6/8 x 27 = 224 | 
 | 0 1110 111 | 7 | 1 7/8 x 27 = 240 | greatest finite number
Infinity | 0 1111 000 | n/a | ∞ | 

## Slide 35: IEEE 754 Encoding Summary
Slide by Bohn
S
E
fraction
S
E = 111…11
fraction
S
E = 000…00
fraction

## Slide 36: IEEE 754 and Integer Hardware
After masking-off sign bit, FP 0 looks like integer 0
After handling special cases, integer comparator works for FP
  Comparison with NaN always returns false
  -0 == 0
  Check sign bits
  Use integer comparator
  Works across full dynamic range from 0 to ∞
Slide by Bohn
Notes: Comparison with NaN always returns false: it’s literally not a number and therefore is not greater than, less than, equal to, nor not equal to any number

## Slide 37: Floating Point Binary Numbers
Rounding

## Slide 38: Floating Point Operations: Compute exactly, then Round
FP arithmetic approximates real arithmetic
  Finite bits  limited range, limited precision
Compute exact result, using as many bits as needed
Make it fit in FP type
  Renormalize; adjust exponent as necessary
    Might overflow/underflow
  Round significand to fit in available bits
Slide by Bohn

## Slide 39: Rounding: Limited Precision
Science class: calculation result cannot be more precise than original data
  Round to appropriate number of significant digits
Binary FP: calculation result cannot be more precise than data type
  Round to fit in available number of bits
Given x, find x' ∈ {x-, x+} ⊆ PermissibleValues, where x- ≤ x ≤ x+
Slide by Bohn

## Slide 40: Rounding: Approaches to Rounding
Typical for real numbers: round x to nearest x'
  What if x is exactly halfway between x- and x+?
Integer types: always round toward zero
  1.9999999 rounds to 1
FP types: four rounding modes
Slide by Bohn

## Slide 41: Rounding: IEEE 754 Rounding Modes
Five rounding modes
  Use functions & constants in <fenv.h> to change modes
Examples with decimal: round to one decimal place (nearest tenth)
raw value 1.34 1.36 1.35 1.45 -1.35
Nearest, even (default) 1.3 1.4 1.4 1.4 -1.4
Nearest, away from zero 1.3 1.4 1.4 1.5 -1.4
Toward zero 1.3 1.3 1.3 1.4 -1.3
Up (toward +∞) 1.4 1.4 1.4 1.5 -1.3
Down (toward -∞) 1.3 1.3 1.3 1.4 -1.4
Slide by Bohn

## Slide 42: Rounding: To Nearest Even
Other modes have statistical biases
Round such that least significant digit is even
More decimal examples: round to two decimal places (nearest hundredth)
2.3451234 2.35 more than halfway: round up
2.3443219 2.34 less than halfway: round down
2.3450000 2.34 halfway: round to nearest even (down)
2.3550000 2.36 halfway: round to nearest even (up)
2.2950000 2.30 halfway: round to nearest even (up)
Slide by Bohn

## Slide 43: Rounding: To Nearest Even, in Binary
Recall: integers are even if and only if LSB is 0
Binary fractional numbers
  “Even”  LSB is 0
  “Less than halfway”  bit to right of LSB is 0
  “Halfway”  bits to right of LSB are 1000…00
  “More than halfway”  bit to right of LSB is 1; OR(remaining bits) = 1
When halfway, round such that LSB is 0
Slide by Bohn

## Slide 44: Rounding: Binary examples
Round to two binary places (nearest fourth)
Raw Raw Rounded Rounded
Decimal Binary Action Binary Decimal
1 11/32 1.010112 < ½way, round down 1.012 1 1/4
1 22/32 1.101102 > ½way, round up 1.112 1 3/4
1 13/32 1.011012 > ½way, round up 1.102 1 2/4
1 20/32 1.101002 ½way, round down 1.102 1 2/4
1 12/32 1.011002 ½way, round up 1.102 1 2/4
1 28/32 1.111002 ½way, round up 10.002 2 0/4
Slide by Bohn

## Slide 45: Rounding: A closer look at “halfway” examples
1 20/32 1.101002 ½way, round down 1.102 1 2/4
  1⅝ is halfway between 1½ and 1¾
  Round down to 1½, to make LSB 0 – subtract 0.0012
1 12/32 1.011002 ½way, round up 1.102 1 2/4
  1⅜ is halfway between 1¼ and 1½
  Round up to 1½, to make LSB 0 – add 0.0012
1 28/32 1.111002 ½way, round up 10.002 2 0/4
  1⅞ is halfway between 1¾ and 2
  Round up to 2, to make LSB 0 – add 0.0012
  Requires re-normalization
    Truncate LSB, increase exponent by 1
Slide by Bohn

## Slide 46: Floating Point Binary Numbers
Arithmetic

## Slide 47: Floating Point Mulitplication
Compute exact product
  Add exponents
  Multiply significands
  XOR sign bits
Renormalize
  If m > 1, logical-right-shift m and increase exponent
  Round fraction to fit
Special cases
  Overflow: ∞
  Underflow: 0
  0 x ∞ = NaN
  NaN x anything = NaN
Slide by Bohn
S
E
fraction
Notes: Multiplication & Division are conceptually easy.
Dividing significands is computationally expensive.
Re“normalize” may place value in subnormal form

## Slide 48: Floating Point Division
Compute exact quotient
  Subtract exponents
  Divide significands
  XOR sign bits
Renormalize
  If 0 < m < 1, left-shift m and decrease exponent
  Round fraction to fit
Special cases
  Overflow: ∞
  Underflow: 0
  ∞ ÷ ∞ = NaN
  0 ÷ 0 = NaN
  NaN ÷ anything = NaN
  anything ÷ NaN = NaN
Slide by Bohn
S
E
fraction
Notes: Multiplication & Division are conceptually easy.
Dividing significands is computationally expensive.
Re“normalize” may place value in subnormal form

## Slide 49: Floating Point Addition
Align binary points
  Assume E1 ≥ E2
  Logical right-shift m2 by E1 ≥ E2
Compute exact sum
  Add (subtract) modified significands
  Exponent is exponent1
Renormalize
Slide by Bohn
S
E
fraction
Notes: Without loss of generality, assume…
Add (subtract) – if one value is positive and other is negative, then subtract
Equation at bottom assumes S1=S2

## Slide 50: Floating Point Subtraction
Slide by Bohn
S
E
fraction
Notes: This really shouldn’t require much explanation: change the sign of the subtrahend, and add.

## Slide 51: Key Ideas
Fixed Point Numbers
  Convert binary fixed point to decimal fixed point using weighted sums
IEEE 754 encoding
  Normal numbers
  Subnormal numbers
  Zero
  Infinity
  NaN
Convert binary fixed point  “scientific notation”  IEEE 754 encoding
Rounding
Floating Point Arithmetic
Slide by Bohn