## Slide 1: Concurrency
Programming at the Hardware/Software Interface

## Slide 2
You are free to:
Share — copy and redistribute the material in any medium or format
Adapt — remix, transform, and build upon the material for any purpose, even commercially
Under the following terms:
Attribution — You must give appropriate credit, provide a link to the license, and indicate if changes were made. You may do so in any reasonable manner, but not in any way that suggests the licensor endorses you or your use.
No additional restrictions — You may not apply legal terms or technological measures that legally restrict others from doing anything the license permits.
Slide by Bohn
This work is licensed under a Creative Commons Attribution 4.0 International License. This work is ©2018-21 Christopher A. Bohn, bohn@unl.edu.
These lecture slides are meant to enhance your use of the Programming at the Hardware/Software Interface textbook. If you have not adopted this publication for your course, please consider doing so.

## Slide 3: Concurrency: Motivation

## Slide 4: Sequential Programming
In CS1/CS2 you were taught sequential programming
First do one thing, then do the next thing…
  Algorithm definition: “…a sequence of steps to…”
Very straight-forward notion of time
  One thing happens at a time
  Step n doesn’t start until step n-1 finishes
Slide by Bohn
Image prepared by Stellar Publishing, obtained from Wikipedia
“Time is what keeps everything from happening at once.”
--Ray Cummings
Artwork by Fantastic Novels, obtained from Wikipedia

## Slide 5: Example: Chat Server One Client
Slide by Bohn
void connect_to_server() {
…
connect(socket_fd, …);
char hostname[BUFFER_SIZE];
gethostname(hostname, BUFFER_SIZE))
send_message(socket_fd, hostname);
}
int accept_connection(int listening_socket_fd) {
…
int accepted_socket_fd =
accept(listening_socket_fd, …);
return accepted_socket_fd;
}
time

## Slide 6: Example: Chat Server One Client
Slide by Bohn
void connect_to_server() {
…
connect(socket_fd, …);
char hostname[BUFFER_SIZE];
gethostname(hostname, BUFFER_SIZE))
send_message(socket_fd, hostname);
}
…
accepted_socket_fd[i] =
accept_connection(listening_socket_fd);
buffer = receive_message(accepted_socket_fd[i], buffer);
printf("Accepted connection from %s.\n", buffer);
strcpy(buffer, "[SERVER]\tPlease type your name.");
send_message(accepted_socket_fd[i], buffer);
…
char *receive_message(int socket_fd, char *message_buffer) {
long number_of_received_bytes =
read(socket_fd, message_buffer, BUFFER_SIZE - 1);
if (number_of_received_bytes < 0) {
perror("Error while receiving message");
number_of_received_bytes = 0;
}
message_buffer[number_of_received_bytes] = '\0';
return message_buffer;
}
void send_message(int socket_fd, char *message) {
if (write(socket_fd, message, strlen(message)) < 0) {
perror("Error while sending message");
}
}

## Slide 7: Interaction with External Systems (and Real World) is Inherently Concurrent
Slide by Bohn
Notes: Three equally-valid interleavings.
Nothing is synchronizing the Client’s write() call and the Server’s accept() call.
Within Client, events happen sequentially: connect, write(hostname), read – read blocks until there’s something to be read, and then write
Within Server, events happen sequentially: accept, read – read blocks until there’s something to be read, and then write (and, not shown, another read)

## Slide 8: Reasoning About Concurrency is Hard!
We (humans) tend to think sequentially
“Time” is misleading
Must (try to) think about all possible sequences of events
  Interleavings
  Error-prone
Slide by Bohn

## Slide 9: Iterative Server Two Clients: Scenario 1
Slide by Bohn
> ./client
Please type the hostname: localhost
Please type the port number: 2310
>
[SERVER] Please type your name.
===============================================
> Stu
[SERVER] Please type your name.
[SERVER] Welcome, Stu.
[SERVER] Stu has joined the chat.
===============================================
>
> ./client
Please type the hostname: localhost
Please type the port number: 2310
[SERVER] Please type your name.
===============================================
> Dee
[SERVER] Please type your name.
[SERVER] Welcome, Dee.
[SERVER] Dee has joined the chat.
===============================================
>
[SERVER] Please type your name.
[SERVER] Welcome, Stu.
[SERVER] Stu has joined the chat.
[SERVER] Dee has joined the chat.
===============================================
>
Notes: “Iterative” Server because it iterates over the clients. First it handles one, then the next, then the next, etc.

## Slide 10: Iterative Server Two Clients: Scenario 2
Slide by Bohn
> ./client
Please type the hostname: localhost
Please type the port number: 2310
>
[SERVER] Please type your name.
===============================================
> Stu
[SERVER] Please type your name.
[SERVER] Welcome, Stu.
[SERVER] Stu has joined the chat.
===============================================
>
> ./client
Please type the hostname: localhost
Please type the port number: 2310
===============================================
>
[SERVER] Please type your name.
===============================================
> Dee
[SERVER] Please type your name.
[SERVER] Welcome, Dee.
[SERVER] Dee has joined the chat.
===============================================
>
[SERVER] Please type your name.
[SERVER] Welcome, Stu.
[SERVER] Stu has joined the chat.
[SERVER] Dee has joined the chat.
===============================================
>
Notes: Nothing forcing synchronization between clients

## Slide 11: Iterative Server Two Clients: Scenario 3
Slide by Bohn
> ./client
Please type the hostname: localhost
Please type the port number: 2310
>
[SERVER] Please type your name.
===============================================
>
[SERVER] Please type your name.
===============================================
> Stu
[SERVER] Please type your name.
[SERVER] Welcome, Stu.
[SERVER] Stu has joined the chat.
===============================================
>
> ./client
Please type the hostname: localhost
Please type the port number: 2310
===============================================
>
[SERVER] Please type your name.
===============================================
> Dee
[SERVER] Please type your name.
[SERVER] Welcome, Dee.
[SERVER] Dee has joined the chat.
===============================================
>
[SERVER] Please type your name.
[SERVER] Welcome, Stu.
[SERVER] Stu has joined the chat.
[SERVER] Dee has joined the chat.
===============================================
>
Notes: The server is blocked from responding to Client 2 while it’s still waiting for Client 1

## Slide 12: Why/Where did Client 2 block?
Call to connect() returns
  Connection not yet accepted
  Server’s TCP manager queues request
Call to write() returns
  Server’s TCP manager buffers data
Call to read() blocks
  Server hasn’t yet called write()
  Nothing yet available to be read
Slide by Bohn
void connect_to_server() {
…
connect(socket_fd, …);
char hostname[BUFFER_SIZE];
gethostname(hostname, BUFFER_SIZE))
send_message(socket_fd, hostname);
}
void *handle_outputs(void *window_arg) {
…
while (running) {
buffer = receive_message(socket_fd, buffer);
wprintw(window, "%s\n", buffer);
…
char *receive_message(int socket_fd, char *message_buffer) {
long number_of_received_bytes =
read(socket_fd, message_buffer, BUFFER_SIZE - 1);
if (number_of_received_bytes < 0) {
perror("Error while receiving message");
number_of_received_bytes = 0;
}
message_buffer[number_of_received_bytes] = '\0';
return message_buffer;
}
void send_message(int socket_fd, char *message) {
if (write(socket_fd, message, strlen(message)) < 0) {
perror("Error while sending message");
}
}

## Slide 13: Reasoning About Concurrency is Very Hard!
Some events are sequential
  A occurs before B
Some events are concurrent
  A could happen before B, or B could happen before A
    Without synchronization, cannot establish order
  We assume no two events occur at the exact same time
    If two events measurably occur at the exact same time, we assume one occurred infinitesimally before the other (but we don’t know beforehand which)
Slide by Bohn
time
concurrent flows
A
B
A
B
A
B
A
B
A
B
C
D
E
F
Notes: A & B on same flow: sequential (A before B)
A & B on different flows, apparently at about the same time: concurrent
A & B on different flows, apparently at different times: concurrent
A & B on different flows, with message between them: sequential (A before B)
Mix of sequential & concurrent
  E before A, B, C, D
  E concurrent with F
  F before B, D
  A before B, C, D
  A concurrent with F
  B before D
  C concurrent with F, B, D

## Slide 14: Common Concurrency Issues
Nondeterminism
Atomicity
Race Conditions
Deadlock
Livelock
Starvation / Fairness
Slide by Bohn

## Slide 15: Improve Responsiveness with Concurrency
Interaction with external systems is inherently concurrent
A server with concurrent flows of control can interact with clients without other blocking clients
Use concurrency whenever you don’t want to force a particular sequence
Slide by Bohn

## Slide 16: Concurrency: Processes

## Slide 17: What’s a Process?
Executable program, resident in memory, possibly holding resources, sometimes executing on the processor
  Has own address space
  Has own context
Slide by Bohn
Stack
Heap
Executable code
Header information and constants
Data Registers
Condition Codes
Stack Pointer
Program Counter
Kernel Context
Process Context
Memory Space

## Slide 18: Creating a New Process to Handle Client
Slide by Bohn
accept(connect_socket_fd, …);
if ((accepted_socket_fd < 0)) {…}
else {
pid_t pid = fork();
if (pid) {
// parent process, listen for the next client
…
} else {
// child process, handle the client
close(connect_socket_fd);
…
manage_client(accepted_socket_fd);
close(accepted_socket_fd);
exit(0);
}
}
time
Notes: Daemon creates new process to handle the client, allows daemon to listen for the next client
(the handler is coded to terminate if the client sends “EXIT” to it)

## Slide 19: What’s Happening Here?
Process ID, or PID
Each process has a unique PID
Slide by Bohn
> ps -u cabohn
PID TTY TIME CMD
70473 ? 00:00:00 systemd
70474 ? 00:00:00 (sd-pam)
70521 ? 00:00:00 sshd
70522 pts/27 00:00:00 tcsh
70544 pts/27 00:00:00 ps
pid_t pid = fork();
if (pid) {
// parent process, listen for the next client
} else {
// child process, handle the client
}

## Slide 20: What’s Happening Here?
fork()
Creates a (nearly) identical process
Full copy of virtual address space
Full copy of open file descriptors
Full copy of process context
Child process completely identical to parent process except
  When fork returns in parent process, it returns child process’s PID
  When fork returns in child process, it returns 0
Slide by Bohn
pid_t pid = fork();
if (pid) {
// parent process, listen for the next client
} else {
// child process, handle the client
}

## Slide 21: Process-Based Server Two Clients: Scenario 3
Slide by Bohn
> ./client
Please type the hostname: localhost
Please type the port number: 2310
>
[SERVER] Please type your name.
===============================================
>
> ./client
Please type the hostname: localhost
Please type the port number: 2310
[SERVER] Please type your name.
===============================================
> Dee
Notes: The server is NOT blocked from responding to Client 2 while it’s still waiting for Client 1

## Slide 22: Process-Based Server Two Clients: Scenario 3
Slide by Bohn
[SERVER] Please type your name.
===============================================
>
[SERVER] Please type your name.
===============================================
> Stu
[SERVER] Please type your name.
[SERVER] Welcome, Stu.
[SERVER] Stu has joined the chat.
===============================================
>
[SERVER] Please type your name.
===============================================
> Dee
[SERVER] Please type your name.
[SERVER] Welcome, Dee.
[SERVER] Dee has joined the chat.
===============================================
>
[SERVER] Please type your name.
[SERVER] Welcome, Dee.
[SERVER] Dee has joined the chat.
yada yada yada
===============================================
>
[SERVER] Please type your name.
[SERVER] Welcome, Dee.
[SERVER] Dee has joined the chat.
yada yada yada
[SERVER] Stu has joined the chat
===============================================
>
Notes: The server is NOT blocked from responding to Client 2 while it’s still waiting for Client 1

## Slide 23: Releasing Unneeded Resources
Slide by Bohn
// child process, handle the client
close(connect_socket_fd); // Close the listening socket file descriptor for this process
close(pipe_to_repeater[0]); // While we're at it, close the reading end of the pipe
for (int i = 0; i < client_list_length; i++) {
close(client_socket_fd_list[i]); // This process certainly doesn't need file
} // descriptors for clients it isn't handling
free(client_socket_fd_list); // The handler doesn't need these lists
free(client_handler_pid_list);
Freeing memory to prevent memory leaks
Freeing file descriptors to prevent resource leaks
This array contains file descriptors for all of the clients except the one this process handles
Notes: Often, the parent would close the “accepted socket” fd, but our particular design requires the parent to maintain an array of open fd’s to each client. Recall that a child gets a copy of all of the open fd’s.
If child doesn’t close the fd’s in the array it has a duplicate of, then by child 40,392 (to make up an arbitrary number), there’ll be 815,736,636 open file descriptors to the clients (plus 40,392 copies of the listening file descriptor)

## Slide 24: Creating, Terminating Processes
int fork(void)
Creates new process
Parent & child are identical copies except
  Different PIDs
  Different fork() return value
void exit(int status)
Terminates current process
Process’s exit status is status
By convention, 0 indicates normal return
Slide by Bohn

## Slide 25: Obtaining a Process’s Exit Status
We can retrieve exit status of process launched from command line
Slide by Bohn
> ./client
Please type the hostname: localhost
Please type the port number: 2310
> echo $?
0
>
> ./server-processes 2310
Server hosted on localhost, listening to port 2310
…
^C[STATUS] Process 30990 received signal 2; notifying client and listener.
[STATUS] Listener process 30986 received signal 2; notifying clients and client handlers.
[STATUS] Process 30990 is terminating with signal 2.
[STATUS] Listener process 30986 is terminating with signal 2.
> echo $?
130
>

## Slide 26: Obtaining a Process’s Exit Status
We can retrieve exit status of process launched from command line
A parent process can block until a child process terminates, and retrieve its exit status
  pid_t wait(int *exit_status)
    Waits for any child process
  pid_t wait_pid(pid_t pid, int *exit_status, int options)
    Waits for a specific child process
  WEXITSTATUS(status)
  See textbook for examples and details; see man -S wait for all details
Slide by Bohn

## Slide 27: Identifying, Changing Processes
pid_t getpid(void)
Returns the PID of the current process
pid_t getppid(void)
Returns the PID of the current process’s parent
int execv(char *path, char *argv[])
int execvp(char *file, char *argv[])
int execl(char *path, char *arg0, ...)
int execlp(char *file, char *arg0, ...)
Replace current process image with new process image
Runs a different program
Slide by Bohn

## Slide 28: Reaping
When process terminates, it still holds resources
  Exit status, unfree()ed memory, open files, etc.
Zombie
  Terminated process that still holds resources
Reaping
  Parent reaps terminated child process via wait() or wait_pid()
    Parent gets child’s exit status
  Kernel deletes process after it has been reaped
If long-running parent process never calls wait() or wait_pid() then zombie processes cause resource leak
Slide by Bohn

## Slide 29: Reaping Example
Slide by Bohn
void wait_demo() {
if (fork()) { // the parent process
if (fork()) {
reap_children();
} else {
sleep_and_exit(1);
}
} else { // the child process
sleep_and_exit(0);
}
}
void reap_children() {
pid_t pid;
int status;
while ((pid = wait(&status)) > 0) {
if (WIFEXITED(status)) {
printf("Process %d terminated with exit status %d.\n",
pid, WEXITSTATUS(status));
} else {
printf("Process %d terminated abnormally.\n", pid);
}
}
if (errno == ECHILD) {
printf("No more children.\n");
} else {
printf("Unexpected error returned by wait().\n");
}
}
time
fork
fork
fork
exit
exit
wait
wait
> ./reap_demo
Process 69579 terminated with exit status 1.
Process 69578 terminated with exit status 0.
No more children.

## Slide 30: Orphan Processes
Processes whose parent terminates before reaping are orphans
Orphaned processes (after terminating) are reaped by init process (pid==1)
Short-running processes can neglect reaping
Long-running processes (shells, servers) must explicitly reap to avoid resource leaks
Slide by Bohn
Notes: Sometimes orphaning a process is intentional, such as when launching a daemon: process forks a child and then terminates, letting the daemon run independently of terminal

## Slide 31: Orphan Example
Slide by Bohn
void orphan_demo() {
if (fork()) {
printf("Parent process (%d) terminating.\n", getpid());
} else {
printf("Child process (%d) running.\n", getpid());
while(1);
}
}
> ./orphan_demo
Parent process (70307) terminating.
Child process (70308) running.
> ps
PID TTY TIME CMD
56904 ttys003 0:01.36 -bash
70308 ttys003 0:03.89 ./orphan_demo
> kill 70308
> ps
PID TTY TIME CMD
56904 ttys003 0:01.37 -bash
>
fork
no-op
Explicitly kill orphaned process, else it will run forever

## Slide 32: Context Switching

## Slide 33: How does concurrency happen?
Hypothesis: can run as many processes as we have processor cores
Slide by Bohn

## Slide 34: How does concurrency happen?
Hypothesis: can run as many processes as we have processor cores
  Impractical for general concurrency
  There are a few special cases in which we’ll map one process to one processor
Context Switching
  Operating system periodically schedules processes to be executed on processor
  Number of scheduled processes bounded by processor cores
Slide by Bohn

## Slide 35: Context Switch
OS Scheduler:
Pauses executing process
Saves executing process’s context to memory
  Registers, stack pointer, program counter, etc.
Selects waiting process to be scheduled for execution
Restores scheduled process’s context from memory
More details in future lesson
Allows concurrency even on computer with one single-core processor
Slide by Bohn
Process 1
Process 2
Processor Core
Executing
Waiting
Waiting
Executing
Context Switch
Context Switch

## Slide 36: Concurrency: Threads

## Slide 37: What’s a Thread?
A “lightweight process”
  A flow of control within a process
  Still has its own flow of control, just like a “heavyweight process”
Shares address space with other threads in same process
Has own context, but…
Thread context is not the same as process context
Slide by Bohn

## Slide 38: Process Context vs Thread Context
Slide by Bohn
Stack
Heap
Executable code
Header information and constants
Data Registers
Condition Codes
Stack Pointer
Program Counter
Kernel Context
Process Context
Memory Space
Heap
Executable code
Header information and constants
Data Registers
Condition Codes
Program Counter
Kernel Context
Stack
Stack Pointer
Thread Context
Shared Memory Space
Each thread has its own stack (to handle its own call chain)
Kernel context (VM structures, file tables, etc) is shared among threads

## Slide 39: Thread = Lightweight Process
Created faster
  No need to duplicate address space
Switched in/out faster
  Smaller unshared context to be saved/restored
Destroyed faster
  Few unshared resources to be reaped
Slide by Bohn

## Slide 40: Creating a New Thread to Handle Client
pthread_create
No child/parent relationship
Each thread has a unique Thread ID, or TID
Thread launches, executing handle_client with argument accepted_socket_fd
  Thread will terminate when handle_client returns
Slide by Bohn
while (running) {
bzero((char *)&client_address, …);
// we don’t want accepted_socket_fd
// on the original thread's stack...
int *accepted_socket_fd = malloc(sizeof(int));
*accepted_socket_fd = accept(connect_socket_fd, …);
pthread_create(&tid, NULL,
handle_client, accepted_socket_fd);
}
Notes: \

## Slide 41: Creating, Terminating Threads
int pthread_create( pthread_t *tid, pthread_attr_t *attr, void *(*start_routine) (void*), void *args)
Create new thread
Set thread attributes via *attr
Thread starts in start_routine
  (*function_name) is a function pointer
Pass argument(s) to start_routine
void pthread_exit( void *retval)
Terminates current thread
Can pass a “return value” via retval pointer
Implicitly called when start_routine returns
Slide by Bohn

## Slide 42: Working with Threads
Slide by Bohn
void *handle_client(void *args) {
int socket_fd = *((int *)args);
free(args);
pthread_detach(pthread_self());
pthread_mutex_lock(&mutex);
add_client(socket_fd, &client_socket_fd_list, 0,
NULL, &client_list_length);
pthread_mutex_unlock(&mutex);
char name[BUFFER_SIZE];
char *buffer = malloc(BUFFER_SIZE);
buffer = receive_message(socket_fd, buffer);
printf("[STATUS]\tAccepted connection from %s.\n", buffer);
strcpy(buffer, "[SERVER]\tPlease type your name.");
send_message(socket_fd, buffer);
buffer = receive_message(socket_fd, buffer);
printf("[STATUS]\tClient identified as %s.\n", buffer);
strncpy(name, buffer, BUFFER_SIZE);
sprintf(buffer, "[SERVER]\tWelcome, %s.", name);
send_message(socket_fd, buffer);
printf("[STATUS]\tThread %ld is listening for messages from %s.\n",
(long)pthread_self(), name);
char *message_to_repeat = malloc(BUFFER_SIZE + strlen(name) + 3);
sprintf(message_to_repeat, "[SERVER]\t%s has joined the chat.",
name);
bool me_running = true;
while (running && me_running) {
pthread_mutex_lock(&mutex);
repeat_message(client_socket_fd_list, client_list_length,
message_to_repeat);
pthread_mutex_unlock(&mutex);
buffer = receive_message(socket_fd, buffer);
sprintf(message_to_repeat, "[%s]\t%s", name, buffer);
if (!strncmp(buffer, "EXIT", 4)) {
printf("%s\n", message_to_repeat);
pthread_mutex_lock(&mutex);
send_message(socket_fd, message_to_repeat);
pthread_mutex_unlock(&mutex);
sprintf(message_to_repeat,
"[SERVER]\t%s has left the chat.",
name);
me_running = false;
}
}
pthread_mutex_lock(&mutex);
remove_client(socket_fd, client_socket_fd_list, NULL);
repeat_message(client_socket_fd_list, client_list_length,
message_to_repeat);
pthread_mutex_unlock(&mutex);
close(socket_fd);
free(message_to_repeat);
free(buffer);
return NULL;
}
Create a copy of file descriptor, free the malloc’d memory

## Slide 43: Working with Threads
Slide by Bohn
void *handle_client(void *args) {
int socket_fd = *((int *)args);
free(args);
pthread_detach(pthread_self());
pthread_mutex_lock(&mutex);
add_client(socket_fd, &client_socket_fd_list, 0,
NULL, &client_list_length);
pthread_mutex_unlock(&mutex);
char name[BUFFER_SIZE];
char *buffer = malloc(BUFFER_SIZE);
buffer = receive_message(socket_fd, buffer);
printf("[STATUS]\tAccepted connection from %s.\n", buffer);
strcpy(buffer, "[SERVER]\tPlease type your name.");
send_message(socket_fd, buffer);
buffer = receive_message(socket_fd, buffer);
printf("[STATUS]\tClient identified as %s.\n", buffer);
strncpy(name, buffer, BUFFER_SIZE);
sprintf(buffer, "[SERVER]\tWelcome, %s.", name);
send_message(socket_fd, buffer);
printf("[STATUS]\tThread %ld is listening for messages from %s.\n",
(long)pthread_self(), name);
char *message_to_repeat = malloc(BUFFER_SIZE + strlen(name) + 3);
sprintf(message_to_repeat, "[SERVER]\t%s has joined the chat.",
name);
bool me_running = true;
while (running && me_running) {
pthread_mutex_lock(&mutex);
repeat_message(client_socket_fd_list, client_list_length,
message_to_repeat);
pthread_mutex_unlock(&mutex);
buffer = receive_message(socket_fd, buffer);
sprintf(message_to_repeat, "[%s]\t%s", name, buffer);
if (!strncmp(buffer, "EXIT", 4)) {
printf("%s\n", message_to_repeat);
pthread_mutex_lock(&mutex);
send_message(socket_fd, message_to_repeat);
pthread_mutex_unlock(&mutex);
sprintf(message_to_repeat,
"[SERVER]\t%s has left the chat.",
name);
me_running = false;
}
}
pthread_mutex_lock(&mutex);
remove_client(socket_fd, client_socket_fd_list, NULL);
repeat_message(client_socket_fd_list, client_list_length,
message_to_repeat);
pthread_mutex_unlock(&mutex);
close(socket_fd);
free(message_to_repeat);
free(buffer);
return NULL;
}
By default, threads are joinable; we’re placing this thread in detached mode
Notes: We’ll get to pthread_mutex_lock and …_unlock later

## Slide 44: Obtaining a Thread’s Return Value
A thread can block until another thread terminates, and retrieve its return value
  Does not have to be the “parent thread” (no such thing)
int pthread_join(pthread_t tid, void **retval)
  Analogous to wait_pid()
Return value set by pthread_exit(void *retval)
Reaps terminated thread’s resources
Slide by Bohn

## Slide 45: Joinable vs Detached Threads
Joinable threads do not release resources until joined
Detached threads release resources as soon as they terminate
Thread calling pthread_join must block until joining thread terminates
  Can force thread to terminate with pthread_kill
Detached threads cannot provide a return value
Chat server doesn’t care when handler threads terminate, doesn’t need return value – run threads in detached mode
Slide by Bohn

## Slide 46: Working with Threads
void *handle_client(void *args) {
…
while (running && me_running) {
pthread_mutex_lock(&mutex);
repeat_message(client_socket_fd_list, client_list_length,
message_to_repeat);
pthread_mutex_unlock(&mutex);
buffer = receive_message(socket_fd, buffer);
sprintf(message_to_repeat, "[%s]\t%s", name, buffer);
if (!strncmp(buffer, "EXIT", 4)) {
printf("%s\n", message_to_repeat);
pthread_mutex_lock(&mutex);
send_message(socket_fd, message_to_repeat);
pthread_mutex_unlock(&mutex);
sprintf(message_to_repeat,
"[SERVER]\t%s has left the chat.",
name);
me_running = false;
}
}
pthread_mutex_lock(&mutex);
remove_client(socket_fd, client_socket_fd_list, NULL);
repeat_message(client_socket_fd_list, client_list_length,
message_to_repeat);
pthread_mutex_unlock(&mutex);
close(socket_fd);
free(message_to_repeat);
free(buffer);
return NULL;
}
Slide by Bohn
void repeat_message(int *client_fd_list, int list_length, char *message) {
printf("%s\n", message);
for (int i = 0; i < list_length; i++) {
if (client_fd_list[i]) {
send_message(client_fd_list[i], message);
}
}
bzero(message, BUFFER_SIZE);
}
Threads use shared memory –
When a socket is added to / removed from client_socket_fd_list, all threads have the update. No need to send a message to a “repeater” thread.
Notes: We’ll get to pthread_mutex_lock and …_unlock later

## Slide 47: Working with Thread
Slide by Bohn
void *handle_client(void *args) {
…
while (running && me_running) {
…
}
pthread_mutex_lock(&mutex);
remove_client(socket_fd, client_socket_fd_list, NULL);
repeat_message(client_socket_fd_list, client_list_length,
message_to_repeat);
pthread_mutex_unlock(&mutex);
close(socket_fd);
free(message_to_repeat);
free(buffer);
return NULL;
}
If this thread doesn’t clean up after itself, it’ll cause a resource leak.

## Slide 48: Synchronizing Access to Shared Resources
If only one thread at a time should have access to a shared variable or resource, use a mutual exclusion token
pthread_mutex_init(pthread_mutex_t *mutex, pthread_mutexattr_t *attr)
pthread_mutex_lock(pthread_mutex_t *mutex)
  If mutex is locked, pthread_mutex_lock blocks until mutex is unlocked
pthread_mutex_unlock(pthread_mutex_t *mutex)
pthread_mutex_destroy(pthread_mutex_t *mutex)
Slide by Bohn

## Slide 49: Process- vs Thread-Based Concurrency
Processes
Clean sharing model
  No shared variables
  No shared file descriptors
  Shares file tables
Simple concurrency model
Additional overhead for process control
Difficult to share data between processes
  FIFO pipes
Threads
Easy to share data between threads
  Shared address space
Insidious bugs due to shared variables
  Subtle, difficult to reproduce
  Sharing might be unintentional!
Overhead for thread control, but more efficient than for processes
Slide by Bohn

## Slide 50: Concurrency: Common Problems

## Slide 51: Common Concurrency Issues
Nondeterminism
Atomicity
Race Conditions
Deadlock
Livelock
Starvation / Fairness
Slide by Bohn

## Slide 52: Using a Shared Variable
Slide by Bohn
int shared_variable = 0;
void *incrementer( void *ignored ) {
for (int i = 0; i < number_of_iterations; i++)
shared_variable++;
return NULL;
}
void *decrementer( void *ignored ) {
for (int i = 0; i < number_of_iterations; i++)
shared_variable--;
return NULL;
}
int main() {
for (int i = 0; i < number_of_pairs; i++) {
incrementer(NULL);
decrementer(NULL);
}
printf("After %d iterations, the shared
variable's value is %d.\n”,
number_of_iterations, shared_variable);
}
Notes: After 1,000,000 iterations, what will the shared variable’s value be?
0

## Slide 53: Using a Shared Variable
Slide by Bohn
int shared_variable = 0;
void *incrementer( void *ignored ) {
for (int i = 0; i < number_of_iterations; i++)
shared_variable++;
return NULL;
}
void *decrementer( void *ignored ) {
for (int i = 0; i < number_of_iterations; i++)
shared_variable--;
return NULL;
}
int main() {
pthread_t tid[2 * number_of_pairs];
for (int i = 0; i < number_of_pairs; i++) {
pthread_create(&tid[2 * i], NULL,
incrementer, NULL);
pthread_create(&tid[2 * i + 1], NULL,
decrementer, NULL);
}
for (int i = 0; i < 2 * number_of_pairs; i++)
pthread_join(tid[i], NULL);
printf("After %d iterations, the shared
variable's value is %d.\n”,
number_of_iterations, shared_variable);
}
Notes: After 1,000,000 iterations, what will the shared variable’s value be?
Who knows? Cannot say for certain. It will change from run to run.
(I recommend that you run chap07/perverse_interleaving.c to demonstrate this)

## Slide 54: Nondeterminism
Given two concurrent events
Cannot determine a priori which will occur first
Cannot determine a priori how much time will lapse between the two events
Given n concurrent events
2n possible interleavings
Slide by Bohn
time
A
B
A
B
A
B

## Slide 55: Atomicity
Atomic operation = indivisible operation, guaranteed to complete without interruption
shared_variable++ comprises three macro-ops or RISC instructions
  ldr – load value from memory
  add – increment value
  str – store value to memory
Slide by Bohn
Notes: Really, atomicity only requires the appearance of no interruption

## Slide 56: Some (but not all) Possible Interleavings
Slide by Bohn
ldr
add
str
ldr
add
str
ldr
add
str
ldr
add
str
ldr
add
str
ldr
add
str
Notes: Most of the interleavings result in a thread updating (and storing) a stale value

## Slide 57: Atomicity
Atomic operation = indivisible operation, guaranteed to complete without interruption
shared_variable++ comprises three macro-ops or RISC instructions
  ldr – load value from memory
  add – increment value
  str – store value to memory
It gets messier:
  Memory accesses are not guaranteed to be atomic!
Slide by Bohn
Notes: Really, atomicity only requires the appearance of no interruption

## Slide 58: Atomic Code
Typical solution: mutual exclusion
  Only one thread at a time can access the shared variable
More general solution
Slide by Bohn
pthread_mutex_t mutex;
void *incrementer( void *ignored ) {
for (int i = 0; i < number_of_iterations; i++) {
pthread_mutex_lock(&mutex);
mutex_shared_variable++;
pthread_mutex_unlock(&mutex);
}
return NULL;
}
void *decrementer( void *ignored ) {
for (int i = 0; i < number_of_iterations; i++) {
pthread_mutex_lock(&mutex);
mutex_shared_variable--;
pthread_mutex_unlock(&mutex);
}
return NULL;
}

## Slide 59: Atomic Code
Atomic operations
  Introduced in C11
Faster than mutex solution if hardware supports atomic memory access
By default enforces sequential memory order
  atomic_fetch_add
Can loosen constraint
  atomic_fetch_add_explicit
Slide by Bohn
#include <stdatomic.h>
atomic_int shared_variable;
void *incrementer(void *ignored) {
for (int i = 0; i < number_of_iterations; i++)
atomic_fetch_add_explicit(&shared_variable, 1,
memory_order_relaxed);
return NULL;
}
void *decrementer(void *ignored) {
for (int i = 0; i < number_of_iterations; i++)
atomic_fetch_sub_explicit(&shared_variable, 1,
memory_order_relaxed);
return NULL;
}

## Slide 60: Atomic Code
Slide by Bohn
> ./atomic_interleaving
After 1000000 sequential iterations, the non-atomic shared variable's value is 0,
and the atomic shared variable's value is 0.
Completed in 0.030534 seconds
After 1000000 concurrent iterations, the non-atomic shared variable's value is 396,
and the mutex'd shared variable's value is 0.
Completed in 0.605536 seconds
After 1000000 concurrent iterations, the non-atomic shared variable's value is -1476,
and the atomic shared variable's value is 0.
Completed in 0.319231 seconds
Notes: “But the sequential code ran faster than the threaded code!” – there is overhead associated with even lightweight context switching (and creating threads), and we are not using concurrency to make the program run faster; we’re using concurrency to make the program more responsive.

## Slide 61: Race Condition
Correct behavior depends on particular interleavings
If incorrect behavior happens rarely, race condition bugs are extremely difficult to reproduce
In production code, most interleavings produce correct behavior
  Otherwise they’d be caught during testing
Race conditions can introduce
  Embarrassing bugs
  Security vulnerabilities
  Lethal bugs
Slide by Bohn
Notes: Canonical case of lethal race condition: Therac-25 (had two lethal race conditions)

## Slide 62: Preventing Race Conditions
Design code that doesn’t admit races
Slide by Bohn
while (running) {
bzero((char *)&client_address, …);
// we don’t want accepted_socket_fd
// on the original thread's stack...
int *accepted_socket_fd = malloc(sizeof(int));
*accepted_socket_fd = accept(connect_socket_fd, …);
pthread_create(&tid, NULL,
handle_client, accepted_socket_fd);
}
void *handle_client(void *args) {
int socket_fd = *((int *)args);
free(args);
pthread_detach(pthread_self());
…
Notes: In the thread-based chat, we made sure that the socket file descriptor isn’t on another thread’s stack, so it can’t be “lost” due to a function return.
In the thread-based chat, we had the handler thread free the memory allocated by the listener thread because the listener thread can’t know when it’s safe to do so.

## Slide 63: Preventing Race Conditions
Design code that doesn’t admit races
Mutual exclusion when necessary
Model checking
Slide by Bohn

## Slide 64: Problems Arising from Mutual Exclusion
Deadlock
  Processes hold resources each other need, cannot progress
Livelock
  Illusion of progress, but no progress is actually made – difficult to detect
  Usually arises from efforts to prevent deadlock
Starvation
  Unfair scheduler can deny resources to a process
  Efforts to prevent deadlock can increase likelihood of starvation
Slide by Bohn

## Slide 65: Parallel Computing

## Slide 66: Multiple Flavors of Parallel Computing
Multiple Instruction, Multiple Data (MIMD)
Multiple flows of control
Each process typically operates on different portion of data
May have shared physical memory (symmetric multiprocessing) or distributed memory
Single Instruction, Multiple Data (SIMD)
One flow of control
Each instruction applied to every element of a data vector
Ideal for data-parallel problems
Slide by Bohn
Notes: Both paradigms saw use into the ‘90s, but the cluster-computing model cemented MIMD for supercomputing since late ‘90s – but SIMD didn’t go away since commodity processors typically have vector processing instructions since late ‘90s/early ‘00s.

## Slide 67: Special Case of Concurrency
Typical Concurrency
Multiple flows of control
  Cooperating processes
Communication & synchronization via messages or shared memory
Goal: responsiveness
Multiple processes share processor
Forks, pthreads library
Parallel Computing (MIMD)
Multiple flows of control
  Subtasks
Communication & synchronization via messages or shared memory
Goal: speed
Typically one process per processor
MPI library, OpenMP library
Slide by Bohn

## Slide 68: Limitations to Parallel Computing
When goal was responsive concurrency, almost no practical limit to responsiveness gains except under abusive scenarios
When goal is faster computing, available performance gains limited by
  Interprocess communication (non-trivial for distributed processors)
  Portion of code that is inherently sequential (cannot be parallelized)
  Available processor cores
    2n processes running on n processor cores can perform no better than n processes running on n processor cores
Slide by Bohn

## Slide 69: Key Ideas
Often use concurrency to improve responsiveness to external systems/people
Process-based concurrency: child process gets copy of parent’s address space
Thread-based concurrency: threads share address space
Concurrent Computing is difficult to get right
  Thinking about concurrency isn’t easy
  Reproducing bugs is challenging
Concurrency opens new types of bugs
  Race conditions, deadlock, livelock
Slide by Bohn