## Slide 1: Concurrency within the Computer System
Programming at the Hardware/Software Interface

## Slide 2
You are free to:
Share — copy and redistribute the material in any medium or format
Adapt — remix, transform, and build upon the material for any purpose, even commercially
Under the following terms:
Attribution — You must give appropriate credit, provide a link to the license, and indicate if changes were made. You may do so in any reasonable manner, but not in any way that suggests the licensor endorses you or your use.
No additional restrictions — You may not apply legal terms or technological measures that legally restrict others from doing anything the license permits.
Slide by Bohn
This work is licensed under a Creative Commons Attribution 4.0 International License. This work is ©2018-21 Christopher A. Bohn, bohn@unl.edu.
These lecture slides are meant to enhance your use of the Programming at the Hardware/Software Interface textbook. If you have not adopted this publication for your course, please consider doing so.

## Slide 3: Accessing I/O Devices with C
Memory-Mapped I/O

## Slide 4: Direct I/O, aka Port-Mapped I/O
Typical
  in dest, src out src, dest
  Copies value from I/O port to memory or general-purpose register
  Copies value from memory or general-purpose register to I/O port
I/O address space distinct from memory address space
Requires additional instructions
Less logic needed to decode address
C must use assembly-code libraries
Slide by Bohn

## Slide 5: Memory-Mapped I/O
I/O device registers reside in memory address space
Any instruction that can use memory can access I/O register
No special instructions needed
Extra complexity in memory bus design
Simplified programming model
  In C, a pointer can point to I/O device register
Slide by Bohn
Notes: A pointer can point to an I/O device register because it’s “just” another address.
If it’s an input register, we’ll want to use the keyword volatile so the compiler doesn’t assume the register’s contents never change (don’t mis-optimize)

## Slide 6: Designs can gravitate to Memory-Mapped I/O
Not a new concept – used in PDP-7
Motorola 68K used memory-mapped I/O exclusively
ATmega368P (used in Arduino Nano) has both Direct-Mapped I/O and Memory-Mapped I/O
  AVR instruction set has 6-bit I/O address space
  64 I/O ports wasn’t enough
  Original I/O registers have both I/O addresses and memory addresses
  Extended I/O registers only have memory addresses
Slide by Bohn

## Slide 7: ATmega368P Data Memory
Slide by Bohn
2KB SRAM
0x08FF
0x0100
0x00FF
0x0060
0x005F
0x0020
0x001F
0x0000
160 Extended I/O Registers
64 I/O Registers
32 General-Purpose Registers
Memory Address
I/O Address
0x3F
0x00
Notes: Surprisingly, even the general-purpose registers are memory-mapped!

## Slide 8: Let’s take a look at Arduino Nano
Three I/O ports (B,C,D)
Each port has three registers
  PINx – Port x’s Input Register
  DDRx – Port x’s Data Direction Register
  PORTx – Port x’s Output Register
Each pin independently set as input/output
Slide by Bohn
D0 (RX)
D1 (TX)
D3
D2
D4
D5
D6
D7
D8
D9
D10
D11
D12
RESET
RESET
D13
A0
A1
A2
A3
A4
A5
A6
A7
PB4
PB3
PB2
PB1
PB0
PD7
PD6
PD5
PD4
PD3
PD2
PD0
PD1
PC6
PB5
PC0
PC1
PC2
PC3
PC4
PC6
PC5

## Slide 9: Pins Can be Input or Output
Use Data Direction Register to set pin as input or output
  Default: input
Input pins can be high impedance or pulled up
  Default: high impedance
High Impedance (Hi-Z) – logic level follows external input
  Common with peripheral input devices, double-throw switches
Pull Up – normally high; becomes low only when external input is low
  Common with single-throw switches
Slide by Bohn
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf
Notes: Datasheets have a LOT of useful information on them!

## Slide 10: Input/Output Registers
Slide by Bohn
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf
UART Transmit/Receive
RESET
Oscillator Inputs
Notes: (click) Some parts of the I/O registers we want to leave alone – Good practice anyway to use bitmasks so you only affect the pins you want to affect, and CowPi isn’t using any of these pins.

## Slide 11: Arduino Core Abstracts-Away These Details
Makes it very easy to program
  No need to think about I/O registers
  Very readable code
Makes code portable to devices with different microcontrollers
  ATmega2560, ARM Cortex-M3, etc
We won’t use these abstractions
  yet
Slide by Bohn
https://www.arduino.cc/reference/en/

## Slide 12: Accessing I/O Registers
#define D8_D13 0 // PINB/DDRB/PORTB
#define A0_A5 1 // PINC/DDRC/PORTC
#define D0_D7 2 // PIND/DDRD/PORTD
uint8_t * const cowpi_IObase = (uint8_t *)0x20;
typedef struct {
volatile uint8_t input; // PINx
volatile uint8_t direction; // DDRx
volatile uint8_t output; // PORTx
} cowpi_ioPortRegisters;
cowpi_ioPortRegisters *gpio = (cowpi_ioPortRegisters *)(cowpi_IObase + 3);
Slide by Bohn

## Slide 13: Accessing I/O Registers
#define D8_D13 0 // PINB/DDRB/PORTB
#define A0_A5 1 // PINC/DDRC/PORTC
#define D0_D7 2 // PIND/DDRD/PORTD
uint8_t * const cowpi_IObase = (uint8_t *)0x20;
typedef struct {
volatile uint8_t input; // PINx
volatile uint8_t direction; // DDRx
volatile uint8_t output; // PORTx
} cowpi_ioPortRegisters;
cowpi_ioPortRegisters *gpio = (cowpi_ioPortRegisters *)(cowpi_IObase + 3);
Slide by Bohn
0x005F
0x0020
I/O Registers
Memory Address
I/O Address
0x3F
0x00

## Slide 14: Accessing I/O Registers
#define D8_D13 0 // PINB/DDRB/PORTB
#define A0_A5 1 // PINC/DDRC/PORTC
#define D0_D7 2 // PIND/DDRD/PORTD
uint8_t * const cowpi_IObase = (uint8_t *)0x20;
typedef struct {
volatile uint8_t input; // PINx
volatile uint8_t direction; // DDRx
volatile uint8_t output; // PORTx
} cowpi_ioPortRegisters;
cowpi_ioPortRegisters *gpio = (cowpi_ioPortRegisters *)(cowpi_IObase + 3);
Slide by Bohn

## Slide 15: Accessing I/O Registers
#define D8_D13 0 // PINB/DDRB/PORTB
#define A0_A5 1 // PINC/DDRC/PORTC
#define D0_D7 2 // PIND/DDRD/PORTD
uint8_t * const cowpi_IObase = (uint8_t *)0x20;
typedef struct {
volatile uint8_t input; // PINx
volatile uint8_t direction; // DDRx
volatile uint8_t output; // PORTx
} cowpi_ioPortRegisters;
cowpi_ioPortRegisters *gpio = (cowpi_ioPortRegisters *)(cowpi_IObase + 3);
Slide by Bohn
cowpi_ioPortRegisters *gpio = (cowpi_ioPortRegisters *)cowpi_IObase + 1;

## Slide 16: Accessing I/O Registers
#define D8_D13 0 // PINB/DDRB/PORTB
#define A0_A5 1 // PINC/DDRC/PORTC
#define D0_D7 2 // PIND/DDRD/PORTD
uint8_t * const cowpi_IObase = (uint8_t *)0x20;
typedef struct {
volatile uint8_t input; // PINx
volatile uint8_t direction; // DDRx
volatile uint8_t output; // PORTx
} cowpi_ioPortRegisters;
cowpi_ioPortRegisters *gpio = (cowpi_ioPortRegisters *)(cowpi_IObase + 3);
Slide by Bohn
gpio[0]
gpio[1]
gpio[2]
gpio[D8_D13]
gpio[A0_A5]
gpio[D0_D7]

## Slide 17: Accessing I/O Registers
Reading from Input
Treat it like any other variable in memory
foo = gpio[D0_D7].input;
Apply bitmask to read a specific bit (or bits)
foo = gpio[D0_D7].input & 0x10;
Writing to Output
Use read-modify-write pattern to change only the intended bits
foo = gpio[D0_D7].output; foo = foo | 0x10; gpio[DO_D7].output = foo;
Or, as one line gpio[DO_D7].output &= ~0x10;
Slide by Bohn
Sets D4 to 1
Sets D4 to 0
Reads D4

## Slide 18: Cow Pi Inputs
Slide by Bohn
SPST momentary pushbuttons
  Set input to Pull-Up
Left button = D8 input
Right button = D9 input
SPDT switches
  Set input to Hi-Z
Left switch = A4 input
Right switch = A5 input
Notes: (The diagram on the left shows us using SPDT switches with the “right” position explicitly pulled high; the current CowPi design treats the switches as SPST and makes use of ATmega328P’s internal pull-up resistors; this is to overcome manufacturing tolerance problems in the small SPDT switches) NEED TO UPDATE THE DIAGRAM AND THE TEXT

## Slide 19: Cow Pi Outputs
External LED = D12 output
Built-in LED = D13 output
Slide by Bohn

## Slide 20: Using Input, Changing Output
uint8_t left_switch, right_switch, left_button, right_button;
void loop() {
left_switch = gpio[A0_A5].input & (1 << 4); // A4
right_switch = gpio[A0_A5].input & (1 << 5); // A5
left_button = gpio[D8_D13].input & 1; // D8
right_button = gpio[D8_D13].input & (1 << 1); // D9
if (left_button) { // button is not pressed
gpio[D8_D13].output &= ~(1 << 4); // turn LED at D12 off
} else {
gpio[D8_D13].output |= (1 << 4); // turn LED at D12 on
}
if (right_switch) {
gpio[D8_D13].output |= (1 << 5); // turn LED at D13 on
} else {
gpio[D8_D13].output &= ~(1 << 5); // turn LED at D13 off
}
}
Slide by Bohn
Polling
Notes: Polling – periodically checking contents of register(s) – simple but requires system to be “always on”
Here, we’re retrieving a value before we act on it (textbook example retrieves value in the `if` condition; for the improved readability, we’re willing to accept the risk that the register changes in the fraction of a microsecond between reading the value and checking the value.

## Slide 21: Input/Output Demonstration
Slide by Bohn

## Slide 22: Other Memory-Mapped Inputs/Outputs Numeric Displays
Slide by Bohn
DE10-Lite Datasheet: https://ftp.intel.com/Public/Pub/fpgaup/pub/Intel_Material/18.1/Computer_Systems/DE10-Lite/DE10-Lite_Computer_NiosII.pdf
Notes: DE10-Lite has 7-segment displays directly mapped to memory

## Slide 23: Other Memory-Mapped Inputs/Outputs Numeric Displays
Slide by Bohn
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf
Notes: Cow Pi uses SPI protocol for 7-segment displays

## Slide 24: Other Memory-Mapped Inputs/Outputs VGA Pixel Buffer
Slide by Bohn
DE10-Lite Datasheet: https://ftp.intel.com/Public/Pub/fpgaup/pub/Intel_Material/18.1/Computer_Systems/DE10-Lite/DE10-Lite_Computer_NiosII.pdf
Notes: I’m pretty sure the y-axis is supposed to be 0..119, not 0..129 since the documentation says the buffer is 160x120.
Some good review of earlier material:
Notice that the pixel buffer is stored in row-major order (see pixel addresses).
Notice that each row occupies 256 elements (really 512 because of that trailing 0) instead of 160 elements. Why? Because we can determine a row’s base address much faster by shifting by 9 than by multiplying by 320.
Might be useful to practice concatenating bitfields – the 8-bit ATmega328 used in the Arduino Nano really doesn’t afford much opportunity to do so, and it’s good to keep it “fresh” in students’ minds.

## Slide 25: Other Memory-Mapped Inputs/Outputs Matrix Keypad
Decoding key presses requires combination of inputs and outputs (covered in lab)
Integrated Circuits exist to decode matrix keypads, deliver BCD input to systems
Slide by Bohn

## Slide 26: Internal Timer/Counters
Arduino Nano has 3 timer/counters
  Timer 0: 8 bit
  Timer 1: 16 bit
  Timer 2: 8 bit
Count from 0 to 0xFF/0xFFFF or to other specified value
Timers 0 & 1 use system clock (16MHz) as frequency source
Timer 2 uses system clock by default but can be changed
Use prescaler to count slower than 16MHz
Slide by Bohn

## Slide 27: Internal Timer/Counters
Timer 0 used for pseudo-real-time clock, counts number of milliseconds since power-up
Counter overflows every 256 beats
Prescaler=64
Increments “time” almost every millisecond
delay(x) idles microcontroller for x milliseconds
millis() returns number of milliseconds since power-up
Slide by Bohn
Notes: Because Timer 0 is used for pseudo-real-time clock, we probably don’t want to mess with it.
(Timers 1 & 2 also have application-specific uses, but the Cow Pi design excludes those applications)
Milliseconds uses uint32_t
There are also delayMicroseconds() and micros(), but I don’t think those’d be very useful for us

## Slide 28: Internal Timer/Counters
Can we make an LED blink the same rate as blink.ino without using delay()?
// blink.ino
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_BUILTIN, HIGH);
delay(1000);
digitalWrite(LED_BUILTIN, LOW);
delay(1000);
}
Slide by Bohn
Notes: This is a blocking implementation – nothing else can happen during the delays

## Slide 29: Internal Timer/Counters
Can we make an LED blink the same rate as blink.ino without using delay()?
  Yes, by using millis() and a bitmask
Not exactly the same rate
  Originally LED was lit for 1000“ms”
    1.024 seconds
  Now LED is lit for 1024“ms”
    1.049 seconds
Can we do it with Timer 2?
uint32_t time;
void setup() {
pinMode(LED_BUILTIN, OUTPUT);
}
void loop() {
time = millis();
if (time & 0x0400)
digitalWrite(LED_BUILTIN, HIGH);
else
digitalWrite(LED_BUILTIN, LOW);
}
Slide by Bohn
Notes: This is a non-blocking implementation – we could have other code outside this if/else that would continue to run and update the system state

## Slide 30: Timer Registers
Slide by Bohn
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf
Notes: For this example, we only need the 8-bit counters

## Slide 31: Accessing Timer Registers
uint8_t * const cowpi_IObase = (uint8_t *)0x20;
typedef struct {
volatile uint16_t control; // TCCRxB TCCRxA
volatile uint8_t counter; // TCNTx
volatile uint8_t compareA; // OCRxA
volatile uint8_t compareB; // OCRxB
} cowpi_timerRegisters8bit;
cowpi_timerRegisters8bit *mytimer0 = (cowpi_timerRegisters8bit *)(cowpi_IObase + 0x24);
cowpi_timerRegisters8bit *mytimer2 = (cowpi_timerRegisters8bit *)(cowpi_IObase + 0x90);
Slide by Bohn

## Slide 32: Let’s see what Timer0’s control register holds
Slide by Bohn

## Slide 33: Let’s see what Timer0’s control register holds
FOC0A, FOC0B “force output compare” must be zero when in PWM mode
COM0A1, COM0A0, COM0B1, COM0B0 “compare output mode” – normal operation, output compare pin disconnected
Slide by Bohn
0 0 0 0 0 0 1 1
0 0 0 0 0 0 1 1
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf

## Slide 34: Timer-Blink
uint32_t time = 0, mytime = 0;
uint8_t now = 0, then = 0;
void setup() {
cowpi_setup(0);
mytimer2->control |= 0x0003; // Mode: Fast PWM
mytimer2->control |= 0x0300; // Prescaler: 64
}
Slide by Bohn
Watch out! Timer2 has different prescaler table
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf

## Slide 35: Timer-Blink
uint32_t time = 0, mytime = 0;
uint8_t now = 0, then = 0;
void setup() {
cowpi_setup(0);
mytimer2->control |= 0x0003; // Mode: Fast PWM
mytimer2->control |= 0x0400; // Prescaler: 64 -- pay attention!
}
void loop() {
time = millis();
then = now;
now = mytimer2->counter;
if (now < then) // overflow?
mytime++;
if (time & 0x0400)
gpio[D8_D13].output |= 0x20;
else
gpio[D8_D13].output &= ~(0x20);
if (mytime & 0x0400)
gpio[D8_D13].output |= 0x10;
else
gpio[D8_D13].output &= ~(0x10);
}
Slide by Bohn
Internal LED
External LED

## Slide 36: Timer-Blink Demonstration
Slide by Bohn

## Slide 37: Exceptional Control Flow
Introduction to Exceptions

## Slide 38: Control Flow / Flow of Control
From startup to shutdown, CPU executes sequence of instructions
Slide by Bohn
pushq %rbp
pushq %rbx
subq $8, %rsp
movl %edi, %ebp
movl $0, %ebx
void count_loop_iterations(int max_iterations) {
int i = 0;
int j;
while (i < max_iterations) {
printf("Loop iteration %d.\n", i);
fflush(stdout);
for (j = 0; j < 100000000; j++);
i++;
}
}

## Slide 39: Control Flow / Flow of Control
jmp …
cmpl $99999999, %eax
jle …
addl $1, %ebx
jmp …
cmpl $99999999, %eax
From startup to shutdown, CPU executes sequence of instructions
Sometimes control flow changes due to jump or branch
Slide by Bohn
pushq %rbp
pushq %rbx
subq $8, %rsp
movl %edi, %ebp
movl $0, %ebx
void count_loop_iterations(int max_iterations) {
int i = 0;
int j;
while (i < max_iterations) {
printf("Loop iteration %d.\n", i);
fflush(stdout);
for (j = 0; j < 100000000; j++);
i++;
}
}

## Slide 40: Control Flow / Flow of Control
From startup to shutdown, CPU executes sequence of instructions
Sometimes control flow changes due to jump or branch
Sometimes control flow changes due to call or return
Slide by Bohn
movl %ebx, %esi
movl $.LC0, %edi
movl $0, %eax
call printf
void count_loop_iterations(int max_iterations) {
int i = 0;
int j;
while (i < max_iterations) {
printf("Loop iteration %d.\n", i);
fflush(stdout);
for (j = 0; j < 100000000; j++);
i++;
}
}
addq $8, %rsp
popq %rbx
popq %rbp
ret

## Slide 41: Control Flow / Flow of Control
From startup to shutdown, CPU executes sequence of instructions
Sometimes control flow changes due to jump or branch
Sometimes control flow changes due to call or return
Jump/Branch/Call/Return introduce changes due to program state
What about system state?
  Data arrives over network
  User hits Control-C
  Illegal memory access
Slide by Bohn

## Slide 42: Exceptional Control Flow
Exceptions
  Control flow change due to system event
  Implemented with hardware & OS
Context switch
  Implemented with hardware timer & OS
Signals
  Implemented by OS
  Signals may be generated due to exceptions or due to programs raising signals
  User-space programs can handle signals
Slide by Bohn

## Slide 43: Exception
Control transferred to OS kernel due event
  Division by zero
  Page fault
  I/O request
  etc
Control given to exception handler
  Each exception type has its own handler
Slide by Bohn
control flow
exception
User Code
Exception Handler
control returns to interrupted instruction or next instruction, or program aborts
Notes: Kernel – portion of OS that is always present in memory

## Slide 44: Exception Table / Interrupt Vector
Exception type has unique exception number
Exception number used to index exception table
  aka, interrupt vector
Exception table stores exception handler addresses
Slide by Bohn
Exception Handler 0
Exception Handler 1
Exception Handler 2
Exception Handler n-1
︙
0
2
1
n-1
…
Exception Table

## Slide 45: Interrupts / Asynchronous Exceptions
Caused by events external to processor
Unpredictable timing – not caused by code being executed
Examples
  Timer
  Arrival of data over network
  Keypress
Handler returns control to next instruction
Slide by Bohn

## Slide 46: Synchronous Exceptions
Trap
  Intentional exception
  Examples: system call, breakpoint trap
  Handler returns control to next instruction
Slide by Bohn
Triggered by instruction being executed

## Slide 47: System Call
syscall assembly instruction
System call number in %rax
  Arguments in %rdi, %rsi, %rdx, %r10, %r8, %r9
  Return value in %rax
  System call numbers found in /usr/include/asm/unistd_64.h
Slide by Bohn

## Slide 48: System Call Examples
Slide by Bohn
#include <stdio.h>
#include <unistd.h>
int main(int argc, char *argv[]) {
write(1, "Before fork.\n", 13);
int pid = 0;
fork();
pid = getpid();
printf("PID = %d\n", pid);
}
.LC0:
.string "Before fork.\n"
.LC1:
.string "PID = %d\n"
main:
subq $8, %rsp
movl $13, %edx
movl $.LC0, %esi
movl $1, %edi
call write
call fork
call getpid
movl %eax, %esi
movl $.LC1, %edi
movl $0, %eax
call printf
movl $0, %eax
addq $8, %rsp
ret
.LC0:
.string "Before fork.\n"
.LC1:
.string "PID = %d\n"
main:
subq $8, %rsp
movq $1, %rdi
movq $.LC0, %rsi
movq $13, %rdx
movq $1, %rax # syscall number for write
syscall
movq $57, %rax # syscall number for fork
syscall
movl %eax, %esi
movl $.LC1, %edi
movl $0, %eax
call printf
movl $0, %eax
addq $8, %rsp
ret
Notes: I used printf at the end because converting integer into string would’ve cluttered the code.
The edits made here bring the system calls to the forefront. The library functions in the original code make system calls.

## Slide 49: Synchronous Exceptions
Trap
  Intentional exception
  Examples: system call, breakpoint trap
  Handler returns control to next instruction
Fault
  Unintentional Exception
  Possibly recoverable
  Recoverable example: page fault
    Handler returns control to current instruction
  Unrecoverable example: segmentation fault
    Handler aborts process
Slide by Bohn
Triggered by instruction being executed

## Slide 50: Page Fault
Attempt to access a memory address not resident in physical memory
Must retrieve memory page from disk
Slide by Bohn
int an_array[500];
int main(int argc, char *argv[]) {
an_array[53] = 19;
}
main:
movl $19, an_array+212(%rip)
movl $0, %eax
ret
control flow
page fault
User Code
Copy page from disk to physical memory
control returns to interrupted instruction

## Slide 51: Segmentation Fault
Attempt to write to read-only memory or to access outside process’s address space
OS signals offending process; if unhandled, process exits abnormally
Slide by Bohn
int an_array[500];
int main(int argc, char *argv[]) {
an_array[5300] = 19;
}
control flow
page fault
User Code
Detect invalid address
send SIGSEGV to process
segmentation fault

## Slide 52: Synchronous Exceptions
Trap
  Intentional exception
  Examples: system call, breakpoint trap
  Handler returns control to next instruction
Abort
  Unintentional exception
  Unrecoverable
  Example: illegal instruction
  Handler aborts process
Fault
  Unintentional Exception
  Possibly recoverable
  Recoverable example: page fault
    Handler returns control to current instruction
  Unrecoverable example: segmentation fault
    Handler aborts process
Slide by Bohn
Triggered by instruction being executed
Notes: We are not going to demonstrate an abort

## Slide 53: Exceptional Control Flow
Handling Interrupts

## Slide 54: What’s the output?
int main( void ) {
…
count_loop_iterations(200);
int *pointer;
pointer = 0;
printf("%d", *pointer);
return 0;
}
Slide by Bohn
void count_loop_iterations(int max_iterations) {
int i = 0;
int j;
while (i < max_iterations) {
printf("Loop iteration %d.\n", i);
fflush(stdout);
for (j = 0; j < 100000000; j++);
i++;
}
}

## Slide 55: Imagine that you’re a process
You’re minding your own business
running a simple, mild-mannered program
moving data around
updating registers and memory
when suddenly, for no apparent reason
Slide by Bohn
Notes: Let this slide build and advance on its own

## Slide 56: Imagine that you’re a process
You’re minding your own business
running a simple, mild-mannered program
moving data around
updating registers and memory
when suddenly, for no apparent reason
a timer interrupt occurs!
Slide by Bohn
Notes: Manually advance this slide

## Slide 57: Imagine that you’re a process
You’re minding your own business
running a simple, mild-mannered program
moving data around
updating registers and memory
when suddenly, for no apparent reason
a timer interrupt occurs!
The interrupt is handled
Slide by Bohn
control flow
timer interrupt
User Code
Exception Handler
Notes: Manually advance this slide

## Slide 58: Imagine that you’re a process
You’re minding your own business
running a simple, mild-mannered program
moving data around
updating registers and memory
when suddenly, for no apparent reason
a timer interrupt occurs!
The interrupt is handled
and our program resumes where it left off
Slide by Bohn
Notes: Let this slide advance and build on its own

## Slide 59: Imagine that you’re a process
You’re minding your own business
running a simple, mild-mannered program
moving data around
updating registers and memory
when suddenly, for no apparent reason
a timer interrupt occurs!
The interrupt is handled
and our program resumes where it left off
as though nothing had happened
Slide by Bohn
Notes: Scenario concludes

## Slide 60: What’s really the output?
int main( void ) {
…
count_loop_iterations(200);
int *pointer;
pointer = 0;
printf("%d", *pointer);
return 0;
}
Slide by Bohn
void count_loop_iterations(int max_iterations) {
int i = 0;
int j;
while (i < max_iterations) {
printf("Loop iteration %d.\n", i);
fflush(stdout);
for (j = 0; j < 100000000; j++);
i++;
}
}

## Slide 61: But… how? What’s causing the extra output?
Slide by Bohn
int main( void ) {
set_timer(1);
sigset(SIGVTALRM, alarm_handler);
sigset(SIGINT, alarm_handler);
sigset(SIGSEGV, memory_access_handler);
count_loop_iterations(200);
int *pointer;
pointer = 0;
printf("%d", *pointer);
return 0;
}
void set_timer(int seconds) {
timer.it_value.tv_sec = seconds;
timer.it_value.tv_usec = 0;
timer.it_interval.tv_sec = seconds;
timer.it_interval.tv_usec = 0;
setitimer(ITIMER_VIRTUAL, &timer, NULL);
}
void alarm_handler(int signal) {
if (signal == 26)
printf(" **** Interrupted by Signal %d (SIGVTALRM) ****\n", signal);
else if (signal == 2)
printf(" **** Interrupted by Signal %d (SIGINT) ****\n", signal);
else
printf(" **** Interrupted by Signal %d (OTHER) ****\n", signal);
}
void memory_access_handler( int signal ) {
printf("You tried to access memory you shouldn’t. Naughty, naughty!\n");
exit(1);
}
Notes: Let this slide build on its own.
Discussion: set a timer, register signal handlers
Used one signal handler for SIGVTALRM and SIGINT; used another for SIGSEGV

## Slide 62: POSIX Signals
SIGNAL NAME NUMBER DESCRIPTION
SIGHUP 1 Hangup
SIGINT 2 Terminal interrupt
SIGQUIT 3 Terminal quit
SIGILL 4 Illegal instruction
SIGTRAP 5 Trace trap
SIGIOT 6 IOT Trap
SIGBUS 7 BUS error
SIGFPE 8 Floating point exception
SIGKILL 9 Kill (can't be caught or ignored)
SIGUSR1 10 User defined signal 1
SIGSEGV 11 Invalid memory segment access
SIGUSR2 12 User defined signal 2
SIGPIPE 13 Write on a pipe with no reader, Broken pipe
SIGALRM 14 Alarm clock
SIGTERM 15 Termination
SIGNAL NAME NUMBER DESCRIPTION
SIGSTKFLT 16 Stack fault
SIGCHLD 17 Child process has stopped or exited, changed
SIGCONT 18 Continue executing, if stopped
SIGSTOP 19 Stop executing (can't be caught or ignored)
SIGTSTP 20 Terminal stop signal
SIGTTIN 21 Background process trying to read, from TTY
SIGTTOU 22 Background process trying to write, to TTY
SIGURG 23 Urgent condition on socket
SIGXCPU 24 CPU limit exceeded
SIGXFSZ 25 File size limit exceeded
SIGVTALRM 26 Virtual alarm clock
SIGPROF 27 Profiling alarm clock
SIGWINCH 28 Window size change
SIGIO 29 I/O now possible
SIGPWR 30 Power failure restart
Slide by Bohn

## Slide 63: But… how? What calls the other code?
Slide by Bohn
control flow
Exception occurs
User Code
Exception Handler
Signal sent to process
Signal handler (default or custom) executes
Control resumes unless signal handler terminated process
Signal
Handler
(user code)

## Slide 64: But… how? Why isn’t count_loop_iterations affected?
Slide by Bohn
control flow
exception
User Code
Kernel
Code
https://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux.git/tree/arch/x86/entry/entry_64.S
Notes: The kernel saves the interrupted process’ context, and restores the context when finished.

## Slide 65: Well, that’s cool
Yes, yes it is
What about the Arduino Nano?
Slide by Bohn

## Slide 66: Arduino Nano Interrupts
We can poll the timer
We can handle timer interrupts
Timer interrupts are more useful than polling the timer
Pseudo-real-time clock updates due to timer overflow interrupt from Timer0
Can we write code to track “milliseconds” using timer interrupts?
Slide by Bohn

## Slide 67: Timer-Blink (Interrupt Version)
uint32_t time = 0;
Volatile uint32_t mytime = 0;
Volatile uint8_t *timer_interrupt_mask = cowpi_IObase + 0x4E;
void setup() {
cowpi_setup(0);
timer_interrupt_mask[0] |= 0x02; // enable "compare match A" interrupt
mytimer0->compareA = 0x80; // compare to 0x80 (halfway between overflows)
}
Slide by Bohn
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf
Notes: We’re making mytime “volatile” since it’ll be updated in one function and read in another – so we don’t want it optimized into a register

## Slide 68: Timer-Blink (Interrupt Version)
ISR(TIMER0_COMPA_vect) {
mytime++;
}
void loop() {
time = millis();
if (time & 0x0400)
gpio[D8_D13].output |= 0x20;
else
gpio[D8_D13].output &= ~(0x20);
if (mytime & 0x0400)
gpio[D8_D13].output |= 0x10;
else
gpio[D8_D13].output &= ~(0x10);
}
Slide by Bohn
avr-libc avr/interrupt.h: https://www.nongnu.org/avr-libc/user-manual/group__avr__interrupts.html
ISR() – creates interrupt handler for specified interrupt vector
TIMER0_COMPA_vect “TimerCounter0 Compare Match A”
ISR() and vectors provided by gcc
Notes: ISR is common term: Interrupt Service Routine
Keep ISRs short! (not necessarily 1-line, but short)

## Slide 69: Arduino Nano Interrupts
Can we write code to interrupt every 1.0 second?
Yes, by resetting counter earlier than natural overflow
Set prescaler to 1024:
  Indistinguishable on human scale, but set compare value to 15,625-1 = 15,624
  The first beat is when counter is 0; the second beat is when counter is 1, etc
Too great for 8-bit timer
But we have a 16-bit timer
Slide by Bohn

## Slide 70: One-Second Interrupt Blink
typedef struct {
volatile uint32_t control;
volatile uint16_t counter;
volatile uint16_t capture;
volatile uint16_t compareA;
volatile uint16_t compareB;
} cowpi_timerRegisters16bit;
struct timer_registers_16bit *mytimer1 = (struct timer_registers_16bit *)(cowpi_IObase + 0x60);
Slide by Bohn
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf

## Slide 71: One-Second Interrupt Blink
void setup() {
cowpi_setup(0);
// Prescaler: 1024
mytimer1->control = 0x500;
// clear timer on compare match
mytimer1->control |= 0x800;
// interrupt (and clear counter) // every 15,625 beats
mytimer1->counter = 0;
mytimer1->compareA = 15624;
timer_interrupt_mask[1] |= 0x02;
}
ISR(TIMER1_COMPA_vect) {
gpio[D8_D13].output ^= 0x10;
}
void loop() {
time = millis();
if (time & 0x0400)
gpio[D8_D13].output |= 0x20;
else
gpio[D8_D13].output &= ~(0x20);
}
Slide by Bohn

## Slide 72: One-Second Interrupt Blink Demonstration
Slide by Bohn
Notes: The external LED is consistently about a half-tick off from the watch’s second hand.
The internal LED starts off similarly out-of-phase, drops into phase with the second hand, drops out, and drops in again.

## Slide 73: Arduino Nano Interrupts
We can poll the timer
We can handle timer interrupts
We can poll the pins
We can handle interrupts from the pins
Slide by Bohn

## Slide 74: ATmega368P Has Two Types of Pin Interrupts
typedef struct {
volatile uint8_t pci_flags;
volatile uint8_t ei_flags;
volatile uint8_t ei_mask;
volatile uint8_t __DO_NOT_TOUCH_1__[0x2A];
volatile uint8_t pci_control;
volatile uint8_t ei_control;
volatile uint8_t __DO_NOT_TOUCH_2__;
volatile uint8_t pci_mask[3];
} pinInterruptRegisters;
Pin Change Interrupt
  Detect logic level change on pins by I/O port (B,C,D)
  If interrupt triggered, need to compare pin register to last known value to determine which had the change
External Interrupt
  Only available for 2 pins
  Can be configured to trigger on any change, rising/falling edge, or logic level
Slide by Bohn

## Slide 75: Going to Higher Level of Abstraction
Pin Change Interrupts must be handled by setting registers and using avr-libc macros
External Interrupts may be handled by setting registers and using avr-libc macros
Arduino Core provides abstraction for external interrupts
  Programmer-friendlier interface
  Allows more-portable code
Slide by Bohn

## Slide 76: Arduino Core External Interrupt Functions
attachInterrupt(digitalPinToInterrupt(pin), isr_function, mode)
detachInterrupt(digitalPinToInterrupt(pin))
Slide by Bohn
https://www.arduino.cc/reference/en/
Converts pin number to interrupt number (optional but recommended)
pin number (2 or 3)
Function to handle interrupt
CHANGE, RISING, FALLING, or LOW
Converts pin number to interrupt number (optional but recommended)
pin number (2 or 3)

## Slide 77: Narcoleptic Blinker
LED blinks
Microcontroller idles after 5 seconds
Wakes on button press
  Either button
Slide by Bohn
ATmega328 Datasheet: https://ww1.microchip.com/downloads/en/DeviceDoc/Atmel-7810-Automotive-Microcontrollers-ATmega328P_Datasheet.pdf
avr-libc avr/sleep.h: https://www.nongnu.org/avr-libc/user-manual/group__avr__sleep.html
Cow Pi pushbuttons
Notes: In hindsight, we would’ve had more sleep options if we used a 74LS21 quad-input AND instead of a 74LS20 quad-input NAND. We can fix that in the future.

## Slide 78: Narcoleptic Blinker
#include <avr/sleep.h>
void go_to_sleep();
void waken();
uint32_t time;
char count = 0;
bool cycled = true;
void setup() {
Serial.begin(9600);
cowpi_setup(0);
}
void loop() {
time = millis();
if (time & 0x100) {
digitalWrite(12, HIGH);
digitalWrite(13, LOW);
if (cycled) {
cycled = false;
count++;
}
} else {
digitalWrite(12, LOW);
digitalWrite(13, HIGH);
cycled = true;
}
if (count == 10) {
count = 0;
go_to_sleep();
}
}
Slide by Bohn

## Slide 79: Narcoleptic Blinker
void go_to_sleep() {
Serial.print("sleep");
digitalWrite(12, LOW); // LED stays lit when CPU sleeps, so turn it off
timer_interrupt_mask[0] &= 0xFE; // Timer0 interrupt wakes CPU from IDLE, so disable it
sleep_enable();
set_sleep_mode(SLEEP_MODE_IDLE);
attachInterrupt(digitalPinToInterrupt(2), waken, FALLING);
sleep_cpu();
}
void waken() {
detachInterrupt(digitalPinToInterrupt(2));
sleep_disable();
timer_interrupt_mask[0] |= 0x01; // Re-enable Timer0 overflow interrupt
digitalWrite(12, HIGH); // Turn LED back on
Serial.println("\tawake");
}
Slide by Bohn

## Slide 80: Narcoleptic Blinker Demonstration
Slide by Bohn
Notes: There must be another external interrupt that sneaks in sometimes (switch bounce?) that causes the CPU to reawaken immediately after going to sleep sometimes. Any other interrupt would’ve left Timer0 interrupts disabled.

## Slide 81: Exceptional Control Flow
Processes

## Slide 82: Processes
Stack
Heap
Executable code
Header information and constants
Data Registers
Condition Codes
Stack Pointer
Program Counter
Kernel Context
Process Context
Memory Space
Instance of a running program
  Not the program itself
  Instance of program, resident in memory, executing (or waiting to execute)
Logical flow of control
  Appears to have exclusive use of processor
  Kernel uses context switching to provide this illusion
Private address space
  Appears to have exclusive use of main memory
  Kernel uses virtual memory to provide this illusion
Slide by Bohn
NOT ALWAYS ILLUSIONS
Sometimes processes really do have (almost) exclusive use of processor and memory
Notes: Examples of situations in which exclusive access to resources isn’t illusionary: microcontrollers, and microprocessors running single-tasking operating systems (e.g., CP/M, MS-DOS). Even then, some context switching is necessary to handle interrupts.

## Slide 83: Illusion of exclusive use of CPU & memory
Slide by Bohn

## Slide 84: Multiprocessing Example
393 processes, 2 of which are active
Identified by Process ID (PID)
Slide by Bohn

## Slide 85: Illusion of Multiprocessing
Many processes run simultaneously, each apparently with its own processor
  Email client, chat client, terminal windows, web browsers…
Slide by Bohn
CPU
CPU
CPU
CPU
CPU
…

## Slide 86: Reality of Multiprocessing
One processor executes many concurrent processes
  Interleaves process executions – multitasking
  Each has its own virtual memory address space – shares physical memory
  Non-executing processes have context saved in memory
Slide by Bohn
Physical Memory
…
CPU
saved
registers
saved
registers
saved
registers
saved
registers
registers

## Slide 87: Context Switch
Outgoing process’s registers, stack pointer, program counter, etc saved to memory
New process selected for execution
Incoming process’s registers & stack pointer restored from memory
Slide by Bohn
Physical Memory
…
CPU
saved
registers
saved
registers
saved
registers
saved
registers
saved
registers
registers

## Slide 88: Multicore Processors
Multiple processor cores on single die
Share physical memory
Each can execute a different process
Slide by Bohn
Physical Memory
…
Core 0
saved
registers
saved
registers
saved
registers
registers
Core 1
registers

## Slide 89: Recall: Context Switch
OS Scheduler:
Pauses executing process
Saves executing process’s context to memory
  Registers, stack pointer, program counter, etc.
Selects waiting process to be scheduled for execution
Restores scheduled process’s context from memory
Allows concurrency even on computer with one single-core processor
Slide by Bohn
Process 1
Process 2
Processor Core
Executing
Waiting
Waiting
Executing
Context Switch
Context Switch

## Slide 90: Context Switch
Similar to exception handling
  Exception handler returns control to same process (or terminate it)
  Context switch returns control to different process
Illusion of never having been interrupted is preserved by saving/restoring process context
Slide by Bohn
control flow
context switch
User Code
User Code
context switch
Kernel Code

## Slide 91: Key Ideas
Input/Output registers often mapped to memory address space
  Not actually part of main memory
Polling: continually checking registers’ contents to determine if action is necessary
Interrupt: asynchronous exception identifies need for action
Fault: exception caused by program’s instruction identifies need for action
Signal: OS construct fired by exception handler or by another process
Context switches look very much like interrupts
  Preserves control flow illusion
Slide by Bohn