## Slide 1: Simple Processor Architecture
Programming at the Hardware/Software Interface

## Slide 2
You are free to:
Share — copy and redistribute the material in any medium or format
Adapt — remix, transform, and build upon the material for any purpose, even commercially
Under the following terms:
Attribution — You must give appropriate credit, provide a link to the license, and indicate if changes were made. You may do so in any reasonable manner, but not in any way that suggests the licensor endorses you or your use.
No additional restrictions — You may not apply legal terms or technological measures that legally restrict others from doing anything the license permits.
Slide by Bohn
This work is licensed under a Creative Commons Attribution 4.0 International License. This work is ©2018-21 Christopher A. Bohn, bohn@unl.edu.
These lecture slides are meant to enhance your use of the Programming at the Hardware/Software Interface textbook. If you have not adopted this publication for your course, please consider doing so.

## Slide 3: A brief discussion on logic circuits

## Slide 4: Digital Signals
Really continuous signals
Use voltage thresholds to assign discrete values
Use transistors designed to transition quickly between “high” voltage and “low” voltage (typically ground)
  Minimize time transitioning through indeterminate-value range
  Transitions from 0 to 1 and from 1 to 0 are not instantaneous!
Slide by Bohn

## Slide 5: Combinatorial & Sequential Logic
Combinatorial Logic – outputs depend only on its current inputs
Sequential Logic – outputs depend on sequence of inputs
Slide by Bohn

## Slide 6: Logic Gates
Respond continuously, with propagation delay
  In combinatorial circuit, delays accumulate
Slide by Bohn
a
a
b
out
out
out = ~a
out = a & b
a
b
out
out = a | b
a
b
out
out = a ^ b
a
b
out
out = ~(a & b)
a
b
out
out = ~(a | b)
a
b
out
out = ~(a ^ b)

## Slide 7: Example Propagation Delay: AND gate
Transistor Technology | Parameter | Typical | Maximum
Baseline (7408) | tPLH | 17.5ns | 27ns
 | tPHL | 12ns | 19ns
Schottky (74S08) | tPLH | 4.5ns | 7ns
 | tPHL | 5ns | 7.5ns
Low-Power Schottky (74LS08) | tPLH | 8ns | 15ns
 | tPHL | 10ns | 20ns
Slide by Bohn
Source: Texas Instruments 74x08 datasheet

## Slide 8: Example Cumulative Delay: Full Adder
45ns from input values being set until all output values are ready (in this hypothetical case)
Outputs take on other, incorrect values before stabilizing
Key reason computers have clocks: give circuits time to stabilize before reading their results
Slide by Bohn
a
b
c_in
a^b
a&b
(a^b)&c_in
sum
c_out

## Slide 9: Every Combinatorial Circuit Implements Some Boolean Expression
a | b | cin | sum | cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
DNF Expressions (sum-of-products):
Slide by Bohn

## Slide 10: Full Adder Implemented in a Programmable Logic Array
DNF Expressions (sum-of-products):
Slide by Bohn

## Slide 11: Multiplexor
A multiplexor (“mux”) is an electronic switch
One input is selected to pass through to output
output = inputs[select]
Slide by Bohn
select
0
1
2
3
.
.
.
n
.
.
.
output
inputs
select
0
1
2
3
.
.
.
n
.
.
.
output
inputs

## Slide 12: Combinatorial & Sequential Logic
Combinatorial Logic – outputs depend only on its current inputs
Sequential Logic – outputs depend on sequence of inputs
  Feedback sequential circuit – ordinary gates and feedback loops
  Clocked synchronous state machine – uses combinatorial logic and feedback sequential circuits to generate outputs that change with respect to a controlling clock signal
  (others also exist)
Slide by Bohn

## Slide 13: Set-Reset Latches
S-R Latch
S | R | Q | /Q
0 | 0 | last Q | last /Q
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
S-R Latch
/S | /R | /Q | Q
1 | 1 | last /Q | last Q
1 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 0 | 1 | 1
Slide by Bohn
_ _
S sets Q to 1
R resets Q to 0
Notes: /S-/R latches more common (use NAND instead of NOR)
I mention S-R latches only because it’s easier to see the semantics

## Slide 14: S-R Latch
/S | /R | /Q | Q
1 | 1 | last /Q | last Q
1 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 0 | 1 | 1
Slide by Bohn
__ __
S
R
Q
Q
_
_
_
Notes: /S = 1, /R = 0: /Q becomes 1, then Q becomes 0, and they stay that way.
/S=1, /R=1: no change
/S=0, /R=1: Q becomes 1, then /Q becomes 0, and then they stay that way.
/S=1, /R=1: no change

## Slide 15: D Latch (“Transparent Latch”)
C | D | Q
0 | 0 | last Q
0 | 1 | last Q
1 | 0 | 0
1 | 1 | 1
Slide by Bohn
D
C
Q
???
D Q
C
Notes: While clock is low, no change to output
When clock goes high, output follows D
When clock goes low, no change to output
When clock goes high, output follows D
If D transitions too close to clock transition, output can be unpredictable – if D went high early enough, output will have transitioned far enough for feedback to carry it high; if D went high too low, output won’t have transitioned very far and will fall low again – need to keep D stable during “t_setup” before clock transition and “t_hold” after clock transition

## Slide 16: Edge-Triggered D Flip-Flop
CLK | D | Q
0 | X | last Q
1 | X | last Q
 | 0 | 0
 | 1 | 1
Slide by Bohn
D Q
C
D Q
C
M
D
CLK
M
Q
D
CLK
Q
D Q
CLK
Notes: When CLK is low, /CLK is high, and M follows D. Q remains unchanged because CLK is low.
When CLK goes high, /CLK is low, and M keeps its value. Q follows M, which was the last value held before CLK went high.
  D’s value is latched into the flip-flop
As CLK remains high, M still holds its value, and Q still follows the unchanging M.
When CLK goes low, M once again follows D. Q remains unchanged.
When CLK goes high, M keeps its value, and Q follows M.
  D’s value is latched into the flip-flop

## Slide 17: Register
Slide by Bohn
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
in7
in6
in5
in4
in3
in2
in1
in0
out7
out6
out5
out4
out3
out2
out1
out0
clk
Latches word of data on rising clock edge

## Slide 18: Register
Saves data
Holds output steady while combinatorial circuit generating input stabilizes
Slide by Bohn
I
I
output
input
I
J
J
J
K
K
K
L
L
L
M
M
M
N
N
N

## Slide 19: 1-cycle-per-instruction processor

## Slide 20: ARM Instruction Encoding
Slide by Bohn
Opcode
Source2
Opcode
Source1
Destination
20 16
9 5
4 0
Register-Register
add x2, x0, x1

## Slide 21: ARM Instruction Encoding
Slide by Bohn
Opcode
Source2
Opcode
Source1
Destination
20 16
9 5
4 0
Register-Register
add x2, x0, 12
Opcode
Source2
Source1
Destination
21 10
9 5
4 0
Register-Immediate

## Slide 22: ARM Instruction Encoding
Slide by Bohn
Opcode
Source2
Opcode
Source1
Destination
20 16
9 5
4 0
Register-Register
str x2, [x1, 24]
Opcode
Source2
Source1
Destination
21 10
9 5
4 0
Register-Immediate
Opcode
Offset
Base Address
Data
20 12
9 5
4 0
Memory Access

## Slide 23: ARM Instruction Encoding
Slide by Bohn
Opcode
Source2
Opcode
Source1
Destination
20 16
9 5
4 0
Register-Register
beq .L3
Opcode
Source2
Source1
Destination
21 10
9 5
4 0
Register-Immediate
Opcode
Offset
Base Address
Data
20 12
9 5
4 0
Memory Access
Opcode
PC Offset
Condition
23 4
3 0
Branch

## Slide 24: ARM Simple Datapath
Slide by Bohn
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK
D Q
CLK

## Slide 25: Observations about this simple design
Stored Program Architecture
  Program counter keeps track of which instruction is being processed
  Each instruction read from the memory, decoded, and executed
  Different types of instructions cause different components to be selected
Separate memories for instructions and data
  Harvard memory model
  Or possibly “modified Harvard” (single address space but partially-distinct instruction & data memories)
Slide by Bohn
Notes: We could say the whole thing is a Harvard architecture, but von Neumann is (rightly or wrongly) given credit for the stored program model
Harvard model allows simultaneous access to instructions and data
Modern workstation & server processors tend to be modified Harvard by having separate instruction & data caches but unified main memory. Microcontrollers had been “pure” Harvard (ROM/EPROM/EEPROM instruction, SRAM data) but introduction of flash memory made it possible to put data in instruction memory – I wouldn’t recommend that you do this except for data that’s accessed only occasionally and (almost) never changes, but you can do it.

## Slide 26: Single-Cycle Design
Each instruction takes the same amount of time as every other instruction
Clock period determined by instruction requiring the most time
No reuse of functional units
Can be used to identify opportunities for hardware reuse (multi-cycle design)
Can be used to identify opportunities for pipelining
Slide by Bohn

## Slide 27: Processor Stages
Fetch instruction from memory (all instructions)
Decode instruction (all instructions)
Read registers (most instructions)
  Often treated as part of Decode or as part of Execute
Execute instruction (most instructions)
  Different instructions use ALU in different ways
Access Memory (only load and store instructions)
Write back to register file (register-register, register-immediate, and load instructions)
Slide by Bohn

## Slide 28: Full Datapath
Slide by Bohn

## Slide 29: Fetch
Slide by Bohn

## Slide 30: Decode
Slide by Bohn

## Slide 31: Execute
Slide by Bohn

## Slide 32: Memory Access
Slide by Bohn

## Slide 33: Writeback
Slide by Bohn

## Slide 34: MIPS Control Logic
Slide by Bohn
 |  | R-format | addi | lw | sw | beq
Inputs | Op5 | 0 | 0 | 1 | 1 | 0
 | Op4 | 0 | 0 | 0 | 0 | 0
 | Op3 | 0 | 1 | 0 | 1 | 0
 | Op2 | 0 | 0 | 0 | 0 | 1
 | Op1 | 0 | 0 | 1 | 1 | 0
 | Op0 | 0 | 0 | 1 | 1 | 0
Outputs | RegDst | 1 | 0 | 0 | x | x
 | ALUSrc | 0 | 1 | 1 | 1 | 0
 | MemtoReg | 0 | 0 | 1 | x | x
 | RegWrite | 1 | 1 | 1 | 0 | 0
 | MemRead | 0 | 0 | 1 | 0 | 0
 | MemWrite | 0 | 0 | 0 | 1 | 0
 | Branch | 0 | 0 | 0 | 0 | 1
 | ALUOp1 | 1 | 0 | 0 | 0 | 0
 | ALUOp0 | 0 | 0 | 0 | 0 | 1
Diagram by Patterson & Hennessey
Instruction[31]
Instruction[30]
Instruction[29]
Instruction[28]
Instruction[27]
Instruction[26]
Not included in logic diagram
Separate adder used for PC

## Slide 35: ARM Instruction Encoding
Slide by Bohn
Opcode
Source2
Opcode
Source1
Destination
20 16
9 5
4 0
Register-Register
Opcode
Source2
Source1
Destination
21 10
9 5
4 0
Register-Immediate
Opcode
Offset
Base Address
Data
20 12
9 5
4 0
Memory Access
Opcode
PC Offset
Condition
23 4
3 0
Branch

## Slide 36: Register-Register Instruction
Slide by Bohn
SIGNAL | VAL
Reg2Sel | 
Src2Sel | 
ALUop | 
WriteMem | 
ReadMem | 
WriteSel | 
WriteReg | 
Branch | 
Opcode
Source2
Opcode
Source1
Destination
20 16
9 5
4 0
0
0
op
0
0
1
1
0

## Slide 37: Register-Register Instruction add x3, x6, x9
Slide by Bohn
SIGNAL | VAL
Reg2Sel | 0
Src2Sel | 0
ALUop | add
WriteMem | 0
ReadMem | 0
WriteSel | 1
WriteReg | 1
Branch | 0
Opcode
Source2
Opcode
Source1
Destination
20 16
9 5
4 0
REGISTER | USE
X3 | 
X6 | 
X9 | 
Next PC | 
Destination
Source 1
Source 2
PC+4

## Slide 38: Register-Immediate Instruction add x5, x2, 125
Slide by Bohn
SIGNAL | VAL
Reg2Sel | 
Src2Sel | 
ALUop | 
WriteMem | 
ReadMem | 
WriteSel | 
WriteReg | 
Branch | 
REGISTER | USE
X5 | 
X2 | 
125 | 
Next PC | 
Opcode
Source2
Source1
Destination
21 10
9 5
4 0

## Slide 39: Memory Access Instruction ldr x9, [x7, 8]
Slide by Bohn
SIGNAL | VAL
Reg2Sel | 
Src2Sel | 
ALUop | 
WriteMem | 
ReadMem | 
WriteSel | 
WriteReg | 
Branch | 
REGISTER | USE
X9 | 
X7 | 
8 | 
Next PC | 
Opcode
Offset
Base Address
Data
20 12
9 5
4 0

## Slide 40: Memory Access Instruction str x1, [x10, 16]
Slide by Bohn
SIGNAL | VAL
Reg2Sel | 
Src2Sel | 
ALUop | 
WriteMem | 
ReadMem | 
WriteSel | 
WriteReg | 
Branch | 
REGISTER | USE
X1 | 
X10 | 
16 | 
Next PC | 
Opcode
Offset
Base Address
Data
20 12
9 5
4 0

## Slide 41: Compare Instruction cmp x3, x15
Slide by Bohn
SIGNAL | VAL
Reg2Sel | 
Src2Sel | 
ALUop | 
WriteMem | 
ReadMem | 
WriteSel | 
WriteReg | 
Branch | 
Opcode
Source2
Opcode
Source1
Destination
20 16
9 5
4 0
REGISTER | USE
X3 | 
X15 | 
Next PC | 

## Slide 42: Branch Instruction beq .L4
Slide by Bohn
SIGNAL | VAL
Reg2Sel | 
Src2Sel | 
ALUop | 
WriteMem | 
ReadMem | 
WriteSel | 
WriteReg | 
Branch | 
REGISTER | USE
Next PC | 
previous instruction compared two unequal values
Offset field = 0x12
Opcode
PC Offset
23 4
3 0

## Slide 43: Branch Instruction beq .L4
Slide by Bohn
SIGNAL | VAL
Reg2Sel | 
Src2Sel | 
ALUop | 
WriteMem | 
ReadMem | 
WriteSel | 
WriteReg | 
Branch | 
REGISTER | USE
Next PC | 
previous instruction compared two equal values
Offset field = 0x12
Opcode
PC Offset
23 4
3 0

## Slide 44: Decoder Logic: Partial Truth Table
i31 | i30 | i29 | i28 | i27 | i26 | i25 | i24 | i23 | i22 | i21 |  | Reg2Sel | Src2Sel | ALUop | WriteMem | ReadMem | WriteSel | WriteReg | Branch
0/1 | - | 0/1 | - | 1 | 0 | 1 | - | - | - | - | Reg-Reg | 0 | 0 |  | 0 | 0 | 1 | 1 | 0
0/1 | 0 | 0/1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | add(r) |  |  | add |  |  |  |  | 0
0/1 | 1 | 0/1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | sub(r) |  |  | sub |  |  |  |  | 0
Slide by Bohn
Notes: It would be helpful to have the block diagram on a second projector.
i31 indicates 32-bit or 64-bit
R-R & R-I: i29 indicates whether flags should be set
R-I: i22 indicates whether immediate value should be left-shifted by 12.
Mem: i30 indicates 32-bit or 64-bit (this is a curious inconsistency with R-R and R-I)
Reg-Reg, or as the ARM Architecture Reference Manual calls it, Data Processing-Register
Add and subtract differ by one bit; this goes straight into the adder’s carry-in

## Slide 45: Decoder Logic: Partial Truth Table
i31 | i30 | i29 | i28 | i27 | i26 | i25 | i24 | i23 | i22 | i21 |  | Reg2Sel | Src2Sel | ALUop | WriteMem | ReadMem | WriteSel | WriteReg | Branch
0/1 | - | 0/1 | - | 1 | 0 | 1 | - | - | - | - | Reg-Reg | 0 | 0 |  | 0 | 0 | 1 | 1 | 0
0/1 | 0 | 0/1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | add(r) |  |  | add |  |  |  |  | 0
0/1 | 1 | 0/1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | sub(r) |  |  | sub |  |  |  |  | 0
0/1 | - | 0/1 | 1 | 0 | 0 | - | - | - | - | X | Reg-Imm | 0 | 1 |  | 0 | 0 | 1 | 1 | 0
0/1 | 0 | 0/1 | 1 | 0 | 0 | 0 | 1 | 0 | 0/1 | X | add(i) |  |  | add |  |  |  |  | 0
Slide by Bohn
Notes: It would be helpful to have the block diagram on a second projector.
i31 indicates 32-bit or 64-bit
R-R & R-I: i29 indicates whether flags should be set
R-I: i22 indicates whether immediate value should be left-shifted by 12.
Mem: i30 indicates 32-bit or 64-bit (this is a curious inconsistency with R-R and R-I)
Reg-Reg, or as the ARM Architecture Reference Manual calls it, Data Processing-Register
Add and subtract differ by one bit; this goes straight into the adder’s carry-in
Reg-Imm, or as the ARM Architecture Reference Manual calls it, Data Processing-Immediate (i30 specified add/sub, just like with R-R)
Look for the similarities between add(i) and add(r) – these suggest the ALUop “add”

## Slide 46: Decoder Logic: Partial Truth Table
i31 | i30 | i29 | i28 | i27 | i26 | i25 | i24 | i23 | i22 | i21 |  | Reg2Sel | Src2Sel | ALUop | WriteMem | ReadMem | WriteSel | WriteReg | Branch
0/1 | - | 0/1 | - | 1 | 0 | 1 | - | - | - | - | Reg-Reg | 0 | 0 |  | 0 | 0 | 1 | 1 | 0
0/1 | 0 | 0/1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | add(r) |  |  | add |  |  |  |  | 0
0/1 | 1 | 0/1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | sub(r) |  |  | sub |  |  |  |  | 0
0/1 | - | 0/1 | 1 | 0 | 0 | - | - | - | - | X | Reg-Imm | 0 | 1 |  | 0 | 0 | 1 | 1 | 0
0/1 | 0 | 0/1 | 1 | 0 | 0 | 0 | 1 | 0 | 0/1 | X | add(i) |  |  | add |  |  |  |  | 0
1 | 0/1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | X | ldr | X | 1 | add | 0 | 1 | 0 | 1 | 0
1 | 0/1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | X | str | 1 | 1 | add | 1 | 0 | X | 0 | 0
Slide by Bohn
Notes: It would be helpful to have the block diagram on a second projector.
i31 indicates 32-bit or 64-bit
R-R & R-I: i29 indicates whether flags should be set
R-I: i22 indicates whether immediate value should be left-shifted by 12.
Mem: i30 indicates 32-bit or 64-bit (this is a curious inconsistency with R-R and R-I)
Reg-Reg, or as the ARM Architecture Reference Manual calls it, Data Processing-Register
Add and subtract differ by one bit; this goes straight into the adder’s carry-in
Reg-Imm, or as the ARM Architecture Reference Manual calls it, Data Processing-Immediate (i30 specified add/sub, just like with R-R)
Look for the similarities between add(i) and add(r) – these suggest the ALUop “add”
Look for the similarities between add(i) and ldr/str – these suggest commonality for adding immediate values

## Slide 47: Decoder Logic: Partial Truth Table
Slide by Bohn
i31 | i30 | i29 | i28 | i27 | i26 | i25 | i24 | i23 | i22 | i21 |  | Reg2Sel | Src2Sel | ALUop | WriteMem | ReadMem | WriteSel | WriteReg | Branch
0/1 | - | 0/1 | - | 1 | 0 | 1 | - | - | - | - | Reg-Reg | 0 | 0 |  | 0 | 0 | 1 | 1 | 0
0/1 | 0 | 0/1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | add(r) |  |  | add |  |  |  |  | 0
0/1 | 1 | 0/1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | sub(r) |  |  | sub |  |  |  |  | 0
0/1 | - | 0/1 | 1 | 0 | 0 | - | - | - | - | X | Reg-Imm | 0 | 1 |  | 0 | 0 | 1 | 1 | 0
0/1 | 0 | 0/1 | 1 | 0 | 0 | 0 | 1 | 0 | 0/1 | X | add(i) |  |  | add |  |  |  |  | 0
1 | 0/1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | X | ldr | X | 1 | add | 0 | 1 | 0 | 1 | 0
1 | 0/1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | X | str | 1 | 1 | add | 1 | 0 | X | 0 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | X | X | X | b.cond | X | X | X | 0 | 0 | X | 0 | 1
0/1 | 0 | 0 | 1 | 0 | 1 | X | X | X | X | X | b/bl | X | X | X | 0 | 0 | X | 0 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0/1 | br/blr | X | X | X | 0 | 0 | X | 0 | 1
Notes: It would be helpful to have the block diagram on a second projector.
R-R & R-I: i31 indicates 32-bit or 64-bit
R-R & R-I: i29 indicates whether flags should be set
R-I: i22 indicates whether immediate value should be left-shifted by 12.
Mem: i30 indicates 32-bit or 64-bit (this is a curious inconsistency with R-R and R-I)
Reg-Reg, or as the ARM Architecture Reference Manual calls it, Data Processing-Register
Add and subtract differ by one bit; this goes straight into the adder’s carry-in
Reg-Imm, or as the ARM Architecture Reference Manual calls it, Data Processing-Immediate (i30 specified add/sub, just like with R-R)
Look for the similarities between add(i) and add(r) – these suggest the ALUop “add”
Look for the similarities between add(i) and ldr/str – these suggest commonality for adding immediate values
Conditional branching and unconditional jump (b/bl/br/blr)’s commonality tells us what sets the branch control value

## Slide 48: Decoder Logic: DNF Expressions
Slide by Bohn
Notes: There may be some refinement as more instructions (and more variations on existing instructions) are added to the logic

## Slide 49: Performance Issues
Infeasible to vary clock period for different instructions
  Could redesign as multiple-cycle-per-instruction processor
Instruction requiring the most time to complete bounds clock period
  Load instruction
  Instruction memory  register file  ALU  data memory  register file
  Memory takes a relatively long time to access
Engineering rule-of-thumb: optimize for the common case
  “Make the common case fast”
  This design violates that principle
We will improve performance by redesigning as pipelined processor
Slide by Bohn
Notes: Store instruction doesn’t necessarily take as long, since the processor can continue executing after putting value on memory bus – doesn’t have to wait for result.
Loads are typically about 25% of executed instructions – not uncommon, but the common case is “not load”

## Slide 50: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining
Slide by Srisa-an

## Slide 51: Key Ideas
Combinatorial, sequential logic
Boolean expression  Combinatorial Circuit
Registers latch in values on clock edge, hold values until next clock edge
ARM instructions: fixed-size instruction word, consistent bitfields simplifies decoding
Control signals can be determined by reasoning about what an instruction does
If you know the binary opcodes, you can design Boolean decoder logic
Slide by Bohn