## Slide 1: Pipelined Processor Architecture
Programming at the Hardware/Software Interface

## Slide 2
You are free to:
Share — copy and redistribute the material in any medium or format
Adapt — remix, transform, and build upon the material for any purpose, even commercially
Under the following terms:
Attribution — You must give appropriate credit, provide a link to the license, and indicate if changes were made. You may do so in any reasonable manner, but not in any way that suggests the licensor endorses you or your use.
No additional restrictions — You may not apply legal terms or technological measures that legally restrict others from doing anything the license permits.
Slide by Bohn
This work is licensed under a Creative Commons Attribution 4.0 International License. This work is ©2018-21 Christopher A. Bohn, bohn@unl.edu.
These lecture slides are meant to enhance your use of the Programming at the Hardware/Software Interface textbook. If you have not adopted this publication for your course, please consider doing so.

## Slide 3: Instruction-Level Parallelism

## Slide 4: Multi-Processing / Multi-Threading
Can improve performance
  “Parallel programming” if extra processor cores are available
  When one thread blocks, other threads can continue (responsiveness)
Must explicitly introduce concurrency
  Difficult to reason about
  Pernicious bugs
  Limited by portion of code that is parallelizable
Slide by Bohn

## Slide 5: Instruction-Level Parallelism
Maintains illusion of sequential programming
  Pro: As “easy” to reason about as a sequential program (because it is)
  Con: If sequential implementation would block, so will ILP
Vector Processing / SIMD
  Classic Cray Supercomputers
  Intel MMX / SSE / SSE2
Very Long Instruction Word (VLIW)
  Intel i860, HP-Intel Itanium
  Relies on compiler
Pipelining
  All x86 after 80486
  Exclusively done in hardware
Slide by Bohn

## Slide 6: Pipelining

## Slide 7: Simple One-Cycle-Per-Instruction Architecture
Slide by Bohn
Clock cycle must be long enough for “load word” instruction:
Fetch instruction
Decode instruction & read from register file
Execute arithmetic (compute address)
Fetch from memory
Write to register file

## Slide 8: By way of analogy…
Time to do a load of laundry with all-in-one washer/dryer:
Fetch dirty laundry
Wash load
Dry load
Fold clean laundry
Slide by Bohn
https://unsplash.com/photos/aJN7zURQ1Wg

## Slide 9: By way of analogy…
Separating the functionality, laundry has independent tasks:
Fetch dirty laundry
Wash load
Dry load
Fold clean laundry
Slide by Bohn
Photo of washer & dryer by Bohn

## Slide 10: Pipeline Concept
Slide by Bohn
Processor has independent tasks:
Fetch instruction
Decode instruction & read from register file
Execute arithmetic (compute address)
Fetch from memory
Write to register file

## Slide 11: Pipelining
Divide process into independent stages
Each load of laundry moves through stages in sequence
At any given time, multiple loads of laundry being processed
Slide by Bohn; screen image by Home Depot
Sixth load
Fifth load
Fourth load
Third load
Second load
First load

## Slide 12: Pipelining
Divide process into independent stages
Each instruction moves through stages in sequence
At any given time, multiple instructions being processed
Slide by Bohn
Second instruction
First instruction
Third instruction
Fourth instruction
Fifth instruction

## Slide 13: Pipeline Stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Generate control signals
  Read program registers
Execute
  Compute result or address
  Determine if branch should be taken
    Compute new PC if so
Memory
  Read or write data memory
Write Back
  Update register file
Slide by Bohn

## Slide 14: Adding Pipeline Registers
Slide by Bohn
  Pipeline registers hold intermediate values from instruction execution
F/D
D/E
E/M
M/W

## Slide 15: Fixing Writeback
Slide by Bohn
F/D
D/E
E/M
M/W

## Slide 16: Pass Control Signals through Pipeline Registers
Slide by Bohn
F/D
D/E
E/M
M/W

## Slide 17: Benefit of Pipelining

## Slide 18: Example Baseline: No Pipelining
Computation requires 320ps
Saving result to register require 25ps (tsetup+thold)
Clock period must be at least 345ps
Slide by Bohn
Combinatorial Logic
25ps
320ps

## Slide 19: Measures of Performance
Latency – time between instruction being issued and result being available
Throughput – number of instructions processed per second
Clock Rate – number of clock cycles per second
Slide by Bohn
Notes: Latency really only matters for the first instruction. Ideally, every instruction after that will finish one cycle after the previous.
Throughput is a much more useful measure.
Clock rate is a horrible measure of performance … as we’ll see.

## Slide 20: Example Baseline: No Pipelining
Computation requires 320ps
Saving result to register require 25ps (tsetup+thold)
Clock period must be at least 345ps
Slide by Bohn
Combinatorial Logic
25ps
320ps

## Slide 21: Example Baseline: No Pipelining
Slide by Bohn
Combinatorial Logic
25ps
320ps

## Slide 22: Instruction n cannot start until Instruction n-1 finishes
Slide by Bohn
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Instruction 5

## Slide 23: Example Baseline: Idealized 4-Way Pipeline
Ideal case: Divide combinatorial logic evenly; each stage requires 80ps
Saving intermediate results to pipeline registers require 25ps
Clock period must be at least 105ps
Slide by Bohn
Stage 1
25ps
25ps
25ps
25ps
80ps
80ps
80ps
80ps
Stage 2
Stage 3
Stage 4

## Slide 24: Example Baseline: Idealized 4-Way Pipeline
Slide by Bohn
Stage 1
25ps
25ps
25ps
25ps
80ps
80ps
80ps
80ps
Stage 2
Stage 3
Stage 4

## Slide 25: Pipelined Instructions have Greater Latency…
Slide by Bohn
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Instruction 5
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D

## Slide 26: Pipelined Instructions have Greater Throughput!
Slide by Bohn
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Instruction 5
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
Up to 4 simultaneous instructions

## Slide 27: Example Baseline: Idealized 4-Way Pipeline
Slide by Bohn
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Instruction 5
CLOCK
A
B
C
D
B
C
D
A
Notes: 0. We start as Instruction 4 is about to issue, and “Instruction 0” is about to retire
With the rising edge of the clock, the intermediate results are latched in to the pipeline registers
During the clock period, the intermediate results are formed in the combinatorial logic

## Slide 28: Non-idealized 4-Way Pipeline
Clock rate set by slowest stage
Faster stages idle while waiting for slowest stage to finish
Slide by Bohn
Stage 1
25ps
25ps
25ps
25ps
90ps
60ps
70ps
100ps
Stage 2
Stage 3
Stage 4

## Slide 29: Non-idealized 4-Way Pipeline
Slide by Bohn
Stage 1
25ps
25ps
25ps
25ps
90ps
60ps
70ps
100ps
Stage 2
Stage 3
Stage 4

## Slide 30: Limitation to Benefits: Faster Stages Sit Idle While Waiting for Slowest Stage to Finish
Slide by Bohn
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Instruction 5
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D
A
B
C
D

## Slide 31: Limitation to Benefits: We Can Divide Combinatorial Logic but Not Registers
# stages | tclock | Throughput
1 | 345ps | 2.90 GIPS
2 | 185ps | 5.41 GIPS
4 | 105ps | 9.52 GIPS
8 | 65ps | 15.38 GIPS
16 | 45ps | 22.22 GIPS
Slide by Bohn
25ps
320ps
25ps
25ps
160ps
160ps
25ps
25ps
25ps
25ps
80ps
80ps
80ps
80ps
25ps
25ps
25ps
25ps
40ps
40ps
40ps
40ps
25ps
25ps
25ps
25ps
40ps
40ps
40ps
40ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
25ps
20 ps
Notes: Increasing pipeline depth increases the clock rate, but the returns diminish even in the ideal case, at the cost of increased circuit complexity. As we’ll see, there are more penalties to be had…

## Slide 32: Pipeline Hazards

## Slide 33: Data Dependences
Data dependences are not bad
Read After Write (RAW)
  Using the result of an earlier calculation
Write After Read (WAR)
  Replacing the value previously stored in a location
Write After Write (WAW)
  Replacing the value previously stored in a location
Slide by Bohn
// C code; p, q are pointers
q = p + 50;
*q = m + n;
// ARM Assembly Code
add x2, x0, 50
add x4, x3, x1
str x4, [x2]
# x86-64 Assembly Code
movq %rdx, 50(%rbx)
addq %rcx, 50(%rbx)
// ARM Assembly Code
add x0, x1, x2
add x1, x0, x3
add x1, x1, x4
# x86-64 Assembly Code
addq %rax, %rbx
addq %rcx, %rax
addq %rdx, %rax
Notes: 0. Data dependences are good things – what would be the point of computing if no calculation relied on the result of an earlier calculation?
RAW – anytime we’re using a value we previously calculated, it’s a RAW dependence – for ARM, the “read” can be source1 or source2 (or a register used to calculate an address), and the “write” can only be destination (“read” can also be the memory location in a load, and ”write” can also be the memory location in a store) – for x86, the “read” can be source or destination (or a register used to calculate an address), and the “write” can only be destination (the more noteworthy part here is that destination is both a read and a write).
WAR – if we used a value and later overwrite it
WAR – if we write a value and later overwrite it

## Slide 34: Data Hazard: Potentially Unsafe Data Dependence
If earlier results are ready to be used, no hazard
Here, the results of the additions are latched into x2 and x4 before the store instruction issues
  No hazard
Slide by Bohn
add x2, x0, 50
add x4, x3, x1
str x4, [x2]

## Slide 35: Data Hazard: Potentially Unsafe Data Dependence
If earlier results are ready to be used, no hazard
Here, the results of the additions are latched into x2 and x4 before the store instruction issues
  No hazard
With instruction-level parallelism, result might not be ready
  Could alter computation
Slide by Bohn
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
W
str x4, [x2]
x2, x4 are written here
x2, x4 are read here

## Slide 36: Data Hazard
Slide by Bohn
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
W
str x4, [x2]
initial values:
x0 = 1000 x1 = 200 x2 = 400 x3 = 20 x4 = 30
1
2
3
4
5
6
7
cycle #
ALU_Result (x2) = 1050
M
ALU_Src1 (x3) = 20
ALU_Src2 (x1) = 200
ALU_Result (x4) = 220
E
ReadData1 (x2) = 400
ReadData2 (x4) = 30
D
cycle 4
should be 1050
should be 220
F/D
D/E
E/M
M/W
Notes: Here is an example showing that the wrong values will be used in the store instruction.
The problem is that we were issuing the store instruction before the results were ready. Maybe we can delay issuing the store instruction…
(Registers in parentheses indicate the source/destination registers for the intermediate values)

## Slide 37: Trying to Fix Data Hazard with a NOP
Slide by Bohn
F/D
D/E
E/M
M/W
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
W
nop
initial values:
x0 = 1000 x1 = 200 x2 = 400 x3 = 20 x4 = 30
1
2
3
4
5
6
7
cycle #
WriteData(x2) = 1050
W
ALU_Result (x4) = 220
M
ReadData1 (x2) = 400
ReadData2 (x4) = 30
D
cycle 5
should be 1050
should be 220
F
D
E
M
W
str x4, [x2]
Notes: NOP = “no op” = “no operation” = “do nothing for one clock cycle”
This doesn’t seem to be enough. Obviously, X4 still isn’t ready, and X2 won’t be ready until the end of cycle 5 – but we need the values at the start of cycle 5.

## Slide 38: Trying to Fix Data Hazard with 2 NOPs
Slide by Bohn
F/D
D/E
E/M
M/W
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
W
nop
initial values:
x0 = 1000 x1 = 200 x2 = 400 x3 = 20 x4 = 30
1
2
3
4
5
6
7
cycle #
WriteData(x4) = 220
W
ReadData1 (x2) = 1050
ReadData2 (x4) = 30
D
cycle 6
should be 220
F
D
E
M
W
str x4, [x2]
F
D
E
M
W
nop
x2 = 1050
Notes: We fixed X2, but we’re still getting the wrong value out of X4

## Slide 39: Fixing Data Hazard with 3 NOPs
Slide by Bohn
F/D
D/E
E/M
M/W
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
W
nop
initial values:
x0 = 1000 x1 = 200 x2 = 400 x3 = 20 x4 = 30
1
2
3
4
5
6
7
cycle #
ReadData1 (x2) = 1050
ReadData2 (x4) = 220
D
cycle 7
F
D
E
M
W
str x4, [x2]
F
D
E
M
W
nop
x2 = 1050
F
D
E
M
W
nop
x4 = 220
Notes: Finally fixed the problem – we now get the correct outcome
Five simultaneous instructions, but here we turned three instructions into six (it won’t always be that bad) – instead of running 5x as fast, we’re running 1.67x as fast.

## Slide 40: Control Dependences: Predicting the PC
Fetch current instruction this clock cycle; fetch next instruction in next clock cycle
If current instruction is conditional branch, cannot determine whether branch is taken until later
If branch/jump target address is saved in a register or memory, cannot determine target address until later
Slide by Bohn

## Slide 41: Simple Prediction Strategy If current instruction…
Does not transfer control
  ARM: next instruction guaranteed to be at PC+4
  x86: next instruction guaranteed to be at %rip+sizeof(current_instr)
Procedure call or unconditional jump to <LABEL>
  Next instruction guaranteed to be at <LABEL>
Conditional Branch
  Predict next PC to be PC+Offset
    Predict “branch taken”
  Only correct if branch is taken
    Typically right 60% of time
Procedure return or jump to address saved in register
  Don’t try to predict
  Cannot predict target address
Slide by Bohn

## Slide 42: Recovering from Misprediction Recovering from Nonprediction
Conditional Branch
  Detect misprediction at end of EXECUTE stage
Procedure Return
  x86: get address from stack (MEMORY)
  ARM: get address from register (DECODE)
Slide by Bohn
E/M

## Slide 43: Unconditional Jump to Address in Register
Slide by Bohn
F
D
E
M
W
F
D
E
M
W
initial values:
x30 = 0x3000
1
2
3
4
5
6
cycle #
ReadData1 (x30) = 0x3000
Jump = 1
D
PC = 0x2004
F
cycle 2
should be 0x3000
0x2000: br x30
0x2004: halt
⋮
0x3000: sub x5, x0, x1
0x2000: ret
F/D
D/E
E/M
M/W
Notes: “br x30” is equivalent to “ret”

## Slide 44: Fixing ARM Nonprediction Control Hazard with 1 NOP
Slide by Bohn
F
D
E
M
W
initial values:
x30 = 0x3000
1
2
3
4
5
6
cycle #
ReadData1 (x30) = 0x3000
Jump = 1
D
PC = 0x3000
F
cycle 3
0x2000: br x30
0x2008: halt
⋮
0x3000: sub x5, x0, x1
F
D
E
M
W
0x2004: nop
F
D
E
M
W
PC=0x3000
F/D
D/E
E/M
M/W
Notes: ARM, the return address (or target address for br instruction) is in a register – available at the end of decode stage / start of execute stage

## Slide 45: Fixing x86 Nonprediction Control Hazard with 3 NOPs
Slide by Bohn
F
D
E
M
W
initial values:
Mem(%rsp) = 0x3000
1
2
3
4
5
6
cycle #
Mem_ReadData1 = 0x3000
Jump = 1
W
PC = 0x3000
F
cycle 5
0x2000: ret
0x2010: halt
⋮
0x3000: sub %r10, %rax
F
D
E
M
W
0x200C: nop
F
D
E
M
W
%rip=0x3000
F
D
E
M
W
0x2004: nop
F
D
E
M
W
0x2008: nop
F/D
D/E
E/M
M/W
Notes: x86, the return address is on the stack – available at end of memory stage / start of writeback stage

## Slide 46: Fixing Conditional Branch
Fix data hazard (cmp setting flags) and control hazard (setting PC correctly)
Slide by Bohn
F
D
E
M
W
F
D
E
M
W
1
2
3
4
5
6
cycle #
Zero = 0 or 1
M
Prev_Zero = 0 or 1
Branch = 1
D
cycle 4
0x2000: cmp x2, x3
0x2008: beq 0x3000
⋮
0x3000: sub x5, x0, x1
F
D
E
M
W
F
D
E
M
W
0x2010: add x5, x0, x1
F
D
E
M
W
0x2004: nop
F
D
E
M
W
0x200C: nop
F/D
D/E
E/M
M/W
Notes: Zero (or other flag) available at end of Execute / start of Memory – need at least three instructions after cmp before potentially-incorrect instruction.
One of these is beq and the other two are NOPs.
At least one of those NOPs needs to be after beq since we won’t have the branch control signal until end of Decode / start of Execute.

## Slide 47: Overcoming Data Hazards: Pipeline Stalls

## Slide 48: Our situation…
We introduced pipelining to improve performance by overlapping instructions
Instructions write their results to registers at the end of the pipeline
Instructions that need results must wait so they can execute correctly
Our compiler introduces NOPs to make that happen
  Making the compiler aware of the pipeline is no worse than VLIW
  The programmer doesn’t need to think about the pipeline
The number of NOPs depends on the instructions and on the pipeline design
Slide by Bohn
and on the pipeline design

## Slide 49: Let’s Compile for a Pipeline that Requires 2 NOPs to overcome a Data Hazard
Slide by Bohn
F
D
E-M
W
add x2, x0, 50
F
D
E-M
W
add x4, x3, x1
F
D
E-M
W
nop
1
2
3
4
5
6
7
cycle #
F
E-M
W
str x4, [x2]
F
D
E-M
W
nop
D
8
mul x5, x6, x7
F
E-M
W
D

## Slide 50: Compatibility Issues
A program compiled for a processor should run without modification on future backwards-compatible processors
If the future processor requires fewer NOPs, our program is fine
If the future processor requires more NOPs, we have a problem
  Example: program compiled for 1-stage processor wouldn’t have enough NOPs for our 5-stage pipeline
  Example: program compiled for 4-stage processor wouldn’t have enough NOPs for our 5-stage pipeline
Slide by Bohn

## Slide 51: 2 NOPs Aren’t Enough When Pipeline Design Needs 3
Slide by Bohn
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
W
nop
initial values:
x0 = 1000 x1 = 200 x2 = 400 x3 = 20 x4 = 30
1
2
3
4
5
6
7
cycle #
WriteData(x4) = 220
W
ReadData1 (x2) = 1050
ReadData2 (x4) = 30
D
cycle 6
should be 220
F
D
E
M
W
str x4, [x2]
F
D
E
M
W
nop
x2 = 1050
8
9
D
E
M
W
mul x5, x6, x7
F

## Slide 52: How Do We Know that Another NOP is Needed?
We know this pipeline needs 3 NOPs to overcome a Data Hazard
The str instruction uses X4
X4 is the destination for an earlier instruction that’s still in the pipeline
The processor can detect this condition!
Slide by Bohn
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
nop
F
D
str x4, [x2]
F
D
E
nop
mul x5, x6, x7
F

## Slide 53: Stalling the Pipeline
Slide by Bohn
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
W
nop
1
2
3
4
5
6
7
cycle #
F
D
E
M
W
str x4, [x2]
F
D
E
M
W
nop
8
9
X4 will be read by this instruction
X4 will be written by this instruction
Processor will inject a “NOP” here
D
E
M
W
mul x5, x6, x7
F

## Slide 54: Stalling the Pipeline
Bubble: hardware-injected NOP
Causes the pipeline to stall behind the bubble
Metaphor: air bubble in water pipe
  Bubble stalls water behind it
  Bubble moves through the pipe
  Water behind the bubble is delayed by the bubble
Slide by Bohn

## Slide 55: Without Stalling the Pipeline
Slide by Bohn
add
mul
nop #1
nop #2
str
mul
add
nop
nop
str
0x4004
0x4000

## Slide 56: Stalling the Pipeline
Slide by Bohn
add
nop #1
nop #2
str
mul
add
nop
nop
str
0x4000
nop
bubble
bubble
bubble
bubble
Notes: Instructions ahead of the bubble continue as before
The D-E pipeline register takes on a NOP (bubble) instead of the str instruction
The pipeline registers behind the decode stage do not latch in the intermediate results for one cycle, preventing instructions behind the bubble from moving forward for one cycle

## Slide 57: Stalling the Pipeline
Slide by Bohn
F
D
E
M
W
add x2, x0, 50
F
D
E
M
W
add x4, x3, x1
F
D
E
M
W
nop
1
2
3
4
5
6
7
cycle #
F
D
E
M
W
str x4, [x2]
F
D
E
M
W
nop
E
M
W
D
pipeline stall
bubble injection
8
9
10
D
E
M
W
mul x5, x6, x7
F
F

## Slide 58: Detecting Stall Condition
Slide by Bohn
E.dest == D.src1 || E.dest == D.src2 || M.dest == D.src1 || M.dest == D.src2
|| W.dest == D.src1 || W.dest == D.src2

## Slide 59: Implementing Stall
Slide by Bohn
Stall Detection
stall
bubble

## Slide 60: Compiler Can Now Ignore Pipeline Design
Stall condition detected whenever a source in Decode stage is a destination in any later stage
  i.e., any earlier instruction still in the pipeline
Stalls 1 cycle if stall condition detected
If stall condition detected in next cycle, will stall another cycle
Slide by Bohn

## Slide 61: Overcome Data Hazard with Pipeline Stalls
Slide by Bohn
F
D
E
M
add x2, x0, 50
F
D
E
add x4, x3, x1
F
D
1
2
3
4
5
6
7
cycle #
str x4, [x2]
F
mul x5, x6, x7
8
9
10
STALL!
D.src1 == M.dest D.src2 == E.dest

## Slide 62: Overcome Data Hazard with Pipeline Stalls
Slide by Bohn
F
D
E
M
add x2, x0, 50
F
D
E
add x4, x3, x1
F
D
1
2
3
4
5
6
7
cycle #
str x4, [x2]
F
mul x5, x6, x7
8
9
10
W
M
E
F
STALL!
D.src1 == W.dest D.src2 == M.dest
D
Notes: Decode & Fetch are stalled. A bubble is injected into Execute.

## Slide 63: Overcome Data Hazard with Pipeline Stalls
Slide by Bohn
F
D
E
M
add x2, x0, 50
F
D
E
add x4, x3, x1
F
D
1
2
3
4
5
6
7
cycle #
str x4, [x2]
8
9
10
W
M
E
D
F
mul x5, x6, x7
F
W
M
E
D
F
STALL!
D.src2 == W.dest
Notes: Decode & Fetch are stalled (again). A bubble is injected into Execute (again). The bubble moves down the pipeline.

## Slide 64: Overcome Data Hazard with Pipeline Stalls
Slide by Bohn
F
D
E
M
add x2, x0, 50
F
D
E
add x4, x3, x1
F
D
1
2
3
4
5
6
7
cycle #
str x4, [x2]
8
9
10
W
M
E
D
W
M
E
F
mul x5, x6, x7
F
F
D
W
M
E
D
F
E
M
W
W
M
W
D
E
M
W
Notes: Decode & Fetch are stalled (yet again). A bubble is injected into Execute (yet again). The bubbles move down the pipeline.
No need for further stalls/bubbles.

## Slide 65: Overcoming Data Hazards: Data Forwarding

## Slide 66: Our situation…
We introduced pipelining to improve performance by overlapping instructions
Instructions write their results to registers at the end of the pipeline
Instructions that need results must wait so they can execute correctly
The pipeline stalls to make that happen
Performance gains are limited by stalls needed for data & control hazards
  Is the added complexity worth the performance benefit?
Slide by Bohn

## Slide 67: Data Forwarding
The problem
  Values written to destination registers at end of Writeback stage
  Values needed from source registers before end of Decode stage
Key insight
  The values exist in the pipeline!
  The values are ready at end of Execute or Memory stage (depending on instruction)
Solution
  Pass values directly from later stages to Decode stage when needed
Slide by Bohn

## Slide 68: Overcome Data Hazard with Data Forwarding
Slide by Bohn
F
D
E
M
add x2, x0, 50
F
D
E
add x4, x3, x1
F
D
1
2
3
4
5
6
7
cycle #
str x4, [x2]
F
mul x5, x6, x7
Data Hazard Detected
D.src1 == M.dest D.src2 == E.dest

## Slide 69: Overcome Data Hazard with Data Forwarding
Slide by Bohn
F
D
E
M
add x2, x0, 50
F
D
E
add x4, x3, x1
F
D
1
2
3
4
5
6
7
cycle #
str x4, [x2]
F
mul x5, x6, x7
W
M
E
D
W
M
W
E
M
W
Notes: Making visual room to show data forwarding (there is no extra time lapsed here)
Because the values that str needs are already in the pipeline, forward these values to the str instruction rather than waiting for the values to be written to the registers
The values still need to continue down the pipeline so that they are, in fact, written to the registers

## Slide 70: Implementing Data Forwarding
Slide by Bohn
Notes: Here, we’re forwarding from the Writeback stage to Decode to show the idea

## Slide 71: Implementing Data Forwarding
Slide by Bohn
Forwarding Logic
  Detects hazard
  Identifies source for src1, src2
  Uses MUX to latch correct value into D/E pipeline register
Notes: Expand that to include forwarding from Memory and from Execute to Decode.
And it needs to forward to both Sources

## Slide 72: Prioritizing Data Forwarding
If more than one stage has a destination that matches the needed source, which stage provides the value?
Preserve non-pipelined semantics
Use the value in the earliest pipeline stage
  The instruction closest to the one needing the value
Slide by Bohn
F
D
E
M
W
add x2, x0, 50
F
D
E
M
mov x2, 100
F
D
E
add x3, x2, x1
1
2
3
4
5
cycle #

## Slide 73: Pipeline Penalties

## Slide 74: Pipeline Stalls are Still Needed
Data Forwarding allows us to use a value as soon as it’s available
Values generated in Execute stage can be forward to instruction immediately behind it
Instructions still must wait for values generated in Memory stage
  But not necessarily as long
Slide by Bohn

## Slide 75: Load/Use Pair
If a value retrieved from memory is used in the very next instruction, the pipeline must stall for 1 cycle
Pipeline-aware compiler may re-order instructions to place an independent instruction between the load and the use
  Only if debugging-level behavior does not have to be preserved
Slide by Bohn
F
D
E
M
W
ldr x2, [x5]
F
D
E
M
W
add x4, x3, x2
D
E
M
W
1
2
3
4
5
6
7
cycle #

## Slide 76: Conditional Branch: Correct Prediction
Assume branch is taken (60% correct)
Load target instruction from target address
Slide by Bohn
F
D
E
M
W
1
2
3
4
5
6
cycle #
0x2000: cmp x2, x3
0x3000: sub x5, x0, x1
F
D
E
M
W
F
D
E
M
W
0x2004: beq 0x3000
7

## Slide 77: Conditional Branch: Recovering from Misprediction
If condition flags indicate branch should not have been taken, we’ll know at the end of the cmp’s Execute stage
Flush the pipeline behind the branch instruction (replace with bubbles)
Load fall-through address into PC
Slide by Bohn
F
D
E
M
W
1
2
3
4
5
6
cycle #
0x2000: cmp x2, x3
0x2008: add x5, x0, x1
F
D
E
M
W
0x2004: beq 0x3000
F
D
E
M
W
7
8
0x3000: sub x5, x0, x1
F
D
E
M
W

## Slide 78: Procedure Return
Must wait until return address is available
Slide by Bohn
F
D
E
M
1
2
3
4
cycle #
0x2000: ret
0x3000: sub x5, x0, x1
F
D
E
F
D
F
D
E
M
W
1
2
3
4
5
6
cycle #
0x2000: ret
0x3000: subq %rdx, %rax
F
D
E
M
W
F
D
F
D
E
M
F
D
E
ARM
x86

## Slide 79: Calculating Performance

## Slide 80: Cycles Per Instruction, and Throughput
Throughput
  Rate at which instructions are processed
  Clock rate divided by Cycles per Instruction
  Earlier, we assumed an instruction finished each clock cycle
Cycles per Instruction (CPI)
  Ideal: an instruction finishes each clock cycle
  Reality: most of the time, an instruction finishes each clock cycle
  Reality: sometimes a bubble “finishes” instead of an instruction
Slide by Bohn

## Slide 81: Calculating CPI
Average penalty for each instruction type: product of
Frequency of instruction occurring in a program
  Example: ldr is about 25% of instructions
Fraction of that instruction’s occurrences that result in a penalty
  Example: 80% of the time, other instructions exist between the load and the use
  Penalty for 20% of ldrs
Number of bubbles injected when the penalty occurs
  Example: When load penalty occurs, 1 bubble is injected
Average load penalty: .25*.20*1 = 0.05
Slide by Bohn

## Slide 82: Calculating CPI
Average total penalty for each instruction type: product of
Fraction of program’s instructions that are the instruction type
  Example: ldr is about 25% of instructions
Fraction of that instruction’s occurrences that result in a penalty
  Example: 80% of the time, other instructions exist between the load and the use
  Penalty for 20% of ldrs
Number of bubbles injected when the penalty occurs
  Example: When load penalty occurs, 1 bubble is injected
Average load penalty: .25*.20*1 = 0.05
Slide by Bohn

## Slide 83: Calculating CPI
Average total penalty: sum of penalties for each instruction type
CPI: ideal CPI plus average total penalty
Slide by Bohn

## Slide 84: Example CPI Calcuation
Slide by Bohn
Instruction | Instruction Frequency | Condition frequency | Stalls/Bubbles | Product
ldr | 0.25 | 0.20 | 1 | 0.05
bXX | 0.20 | 0.40 | 1 | 0.08
ret | 0.02 | 1.00 | 3 | 0.06
Total Penalty |  |  |  | 0.19

## Slide 85: Comparing Designs
Slide by Bohn
Instruction | Instruction Frequency | Condition frequency | Stalls/Bubbles | Product
ldr | 0.25 | 0.20 | 1 | 0.05
bXX | 0.20 | 0.40 | 2 | 0.16
ret | 0.02 | 1.00 | 1 | 0.02
Total Penalty |  |  |  | 0.23
Let’s try a different design that reduces the return penalty from 3 to 1 but increases the branch penalty from 1 to 2 – is this an improvement?

## Slide 86: Comparing Branch Prediction Strategies
Slide by Bohn
Instruction | Instruction Frequency | Condition frequency | Stalls/ Bubbles | Product
ldr | 0.25 | 0.20 | 2 | 0.10
bXX | 0.20 | 0.40 | 1 | 0.08
ret | 0.02 | 1.00 | 1 | 0.02
Total Penalty |  |  |  | 0.20
Instruction | Instruction Frequency | Condition frequency | Stalls/ Bubbles | Product
ldr | 0.25 | 0.20 | 2 | 0.10
bXX | 0.20 | 0.35 | 1 | 0.07
ret | 0.02 | 1.00 | 1 | 0.02
Total Penalty |  |  |  | 0.19
Predict Taken
Correct 60% of the time
Predict Backwards Taken, Forward Not Taken (BTFNT)
Correct 65% of the time
Is the performance gain worth the design complexity?
Notes: Sometimes it’s not a question of which design has better performance, but it’s a tradeoff: better performance vs more complex design or extra power / heat dissipation requirements.
Here we’ll assume a pipeline that has two memory stages to compensate for slower memory, allowing for a faster clock (but a greater load/use penalty).
What is the penalty? What is the CPI?
BTFNT recognizes that loops almost always branch to the target (every iteration except the last one) but more often than not, programmers write if statements expecting the then block to execute so we don’t want to assume that we should branch to the else target.
What is the condition frequency for branches now? If we’re correct 65 of the time, how often are we wrong?
What’s the penalty & CPI?
Is the performance gain worth the extra design complexity? Probably. It’s a small gain, but the cost is only an extra adder, and we’d only be interested in the sign bit after comparing the current PC and the potential target.

## Slide 87: Very Advanced Architecture

## Slide 88: Out of Order Execution
Compiler can rearrange instructions to prevent stalls
  But only if it knows pipeline design: which hazards require stalls, and how many bubbles
Dynamic scheduling: use hardware algorithm to execute/retire instructions when safe to do so
  Instructions need not execute in fetch order
Slide by Bohn

## Slide 89: Out of Order Execution: Scoreboarding
Introduced in CDC 6600
Uses dependency graph to manage RAW, WAR hazards
Uses DAG to manage WAW hazards
Stall instructions at various stages until dependences are resolved
Other instructions with resolved hazards may proceed while another is stalled
Slide by Bohn

## Slide 90: Out of Order Execution: Tomasulo Algorithm
Introduced in IBM 360/Model 91
Renames actual registers in instruction with logical registers
  Eliminate false data dependences
Instructions issued to reservation station
  Buffer for instructions waiting for dependences to be resolved
Instruction sent to execution unit when dependences are resolved and unit is available
Slide by Bohn

## Slide 91: Superscalar Architecture
“Multiple pipelines”
Achieve CPI below 1.0
Issue multiple instructions each clock cycle (like VLIW)
Multiple execution units
Example: ARM Cortex A75 each core has:
3 instructions issued per cycle
2 integer ALUs
2 SIMD/FP units
2 load/store units
1 branch predictor
Slide by Bohn

## Slide 92: Branch Prediction
High-Performance Branch Prediction – Critical to Performance
  Deeper pipelines  increased ideal throughput
  Deeper pipelines  greater misprediction penalty
Use state machine or matrix to track each branch’s taken/not taken history – find patterns
  First encounter: use BTFNT
  Subsequent encounters: predict based on recent pattern
Branch Target Buffer
  Instead of predicting taken/not taken, predict next instruction’s address
Slide by Bohn

## Slide 93: Return Stack Buffer
Maintain small stack of return addresses
  Accessible immediately, no bubbles required
Mirrors return addresses in program stack / return address register
Typically 4-16 entries – deep enough for most applications
If address from RSB doesn’t match “official copy” then flush pipeline
Slide by Bohn

## Slide 94: Return Stack Buffer
Slide by Bohn
RSB

## Slide 95: Key Ideas
Pipelining improves performance while preserving sequential semantics
Pipeline registers store intermediate results between pipeline segments
Data dependencies & control dependencies always exist
  Dependencies that could cause pipeline to produce incorrect result are hazards
Hazards limit pipeline benefits
  Bubbles placed in pipeline due to pipeline stalls & pipeline flushes
Data forwarding eliminates/reduces stalls
Throughput (instructions per second) more meaningful than clock cycle
CPI demonstrates deviation from ideal throughput
Slide by Bohn